## Slide 1
Lessons Learned
From
On-Orbit Anomaly Research
On-Orbit Anomaly Research
NASA IV&V Facility
Fairmont, WV, USA
2013 Annual Workshop on Independent Verification & Validation of Software
Fairmont, WV, USA
September 10-12, 2013

## Slide 2: Agenda
Introduction
  On-Orbit Anomaly Research (OOAR)
  Presentation Objective and Organization
Anomalies
  Pseudo-Software – Command Scripts
  Software and Hardware Interface
  Data Storage and Fragmentation
  Communication Protocols
  Sharing of Resources – CPU
OOAR Contact Information

## Slide 3: Introduction
On-Orbit Anomaly Research (OOAR)
  Primary goals:
    Study NASA post-launch anomalies and provide recommendations to improve IV&V processes, methods, and procedures
    Brief IV&V analysts on new and emerging technologies, as applied to space mission software, and on how to identify potential software issues related to them

## Slide 4: Introduction
Presentation Objective and Organization
  Present IV&V lessons learned from selected on-orbit anomalies
  Anomalies representative of some of common “themes” observed in post-launch software problems
  Five themes represented

## Slide 5: Introduction
Presentation Objective and Organization (Cont’d)
  Five common anomaly themes represented:
    Pseudo-Software – Command Scripts
    Software and Hardware Interface
    Data Storage and Fragmentation
    Communication Protocols
    Sharing of Resources – CPU

## Slide 6: Introduction
Presentation Objective and Organization (Cont’d)
  Topics covered:
    Anomaly Description
    Background Information
    Cause of Anomaly
    Project’s Solution
    Observations
    IV&V Lessons

## Slide 7: Anomaly: Pseudo-Software – Command Scripts
Anomaly Description
  Measurement device on science instrument disabled at start of blackout period
  Command to re-enable device at end of blackout period failed
  Failure leading to loss of science data

## Slide 8: Anomaly: Pseudo-Software – Command Scripts
Background Information
  Two measurement devices 1 and 2 on science instrument
  Only one device active at any given time
  Blackout period imposed on active device to protect against damage from environment
  Active device commanded by ground software to be disabled at start of blackout period
  Active device commanded by ground software to be re-enabled at end of blackout period

## Slide 9: Anomaly: Pseudo-Software – Command Scripts
Background Information (Cont’d)
  Disable and enable commands part of a command script
  Flaw in command script:
    Commands labeled for device 1 only
  FSW fault management feature A:
    Process disable command for any active device even if command labeled incorrectly
    To protect active device during blackout period

## Slide 10: Anomaly: Pseudo-Software – Command Scripts
Background Information (Cont’d)
  FSW fault management feature B:
    Do not process re-enable command if mislabeled for inactive device
    To protect against occurrence of lower-level software error:
      Not possible to re-enable an inactive device

## Slide 11: Anomaly: Pseudo-Software – Command Scripts
Cause of Anomaly
  Device 2 active
  Disable command mislabeled for (inactive) device 1
  FSW disabled device 2 anyway
  Re-enable command also mislabeled for (inactive) device 1
  FSW rejected re-enable command
  Active device 2 staying disabled; no science data collected

## Slide 12: Anomaly: Pseudo-Software – Command Scripts
Project’s Solution
  Manually commanded (active) device 2 to be re-enabled and resume operations

## Slide 13: Anomaly: Pseudo-Software – Command Scripts
Observations
  Anomaly due to flaw in command script used by ground software
  FSW not at fault
  FSW fault management averted a more-serious anomaly by processing mislabeled disable command:
    Active device 2 could have been damaged if not disabled

## Slide 14: Anomaly: Pseudo-Software – Command Scripts
Observations (Cont’d)
  FSW fault management could not stop anomaly at end of blackout period
  Instead, designed to protect against another software error
  Ground software or mission operators in better position to have caught the flaw in command script. However,
    no ground software fault management provision
    mission operators not alert enough

## Slide 15: Anomaly: Pseudo-Software – Command Scripts
IV&V Lessons
  If ground software in scope for IV&V analysis, insist on ground software to detect and protect against faults in “pseudo-software,” e.g., command scripts
    IV&V not usually around for software operation
    Mission operators not reliable enough due to various factors (training, alertness, performance consistency, etc.)

## Slide 16: Anomaly: Pseudo-Software – Command Scripts
IV&V Lessons (Cont’d)
  If ground software out of scope for IV&V analysis, identify and report potential sources of error in ground software interfacing with FSW
    Result of interface analysis of FSW
    Caveats:
      Not rigorous conventional IV&V issues
      IV&V not able to track issues to resolution (not around for software operation)
      New concept in IV&V

## Slide 17: Anomaly: Software and Hardware Interface
Anomaly Description
  Antenna on spacecraft commanded to re-orient by rotating in delta-angle increments
  Fault protection maximum limit for delta-angle tripped
  Antenna rotation suspended in mid-maneuver

## Slide 18: Anomaly: Software and Hardware Interface
Background Information
  Antenna on spacecraft re-oriented through nominal 14-deg. increments of rotation
  FSW capable of commanding increments of rotation larger than 14 deg.
  Fault protection imposing limit of 14-deg. increments on FSW for mechanical stability

## Slide 19: Anomaly: Software and Hardware Interface
Background Information (Cont’d)
  FSW counter keeping track of 14-deg. increments
  Electro-mechanical switch sending signal to increment or decrement counter:
    Increment by 1 for “forward” rotation signal
    Decrement by 1 for “backward” rotation signal
  Switch sending signal at end of 14-deg. rotations when forward or backward contact made

## Slide 20: Anomaly: Software and Hardware Interface
Cause of Anomaly
  Antenna structure “wiggled” at end of one 14-deg. rotation after coming to a halt
    Back and forth motion due to structure’s elasticity and its momentum exchange with attached linkage
  Switch correctly sent “forward” signal first, incrementing FSW counter by 1
  Switch incorrectly sent “backward” signal next, decrementing FSW counter by 1

## Slide 21: Anomaly: Software and Hardware Interface
Cause of Anomaly (Cont’d)
  Net effect: No change in counter’s value at end of 14-deg. rotation
  FSW, monitoring counter, assuming latest command to rotate by 14 deg. having failed
  FSW compensating by commanding a 28-deg. rotation next time
  Fault protection max. limit of 14-deg. rotation tripped
  Antenna rotation maneuver suspended

## Slide 22: Anomaly: Software and Hardware Interface
Project’s Solution
  Remove max. limit of 14-deg. rotations from fault protection

## Slide 23: Anomaly: Software and Hardware Interface
Observations
  Removing fault protection inhibit of 14-deg.:
    Not addressing root cause of anomaly
    Removing a legitimate fault protection feature and making antenna vulnerable to other faults
  Phenomenon causing anomaly well understood and known as “switch bounce”
  Possible solutions to switch bounce:
    Take multiple samples of contact state
    Introduce time delay in taking switch output

## Slide 24: Anomaly: Software and Hardware Interface
IV&V Lessons
  Have a deep understanding of characteristics of hardware interfacing with software
  Apply this understanding to software analysis of requirements, design, and tests

## Slide 25: Anomaly: Data Storage and Fragmentation
Anomaly Description
  “Write” operations to store data on a spacecraft’s data storage device failed
  Multiple buffers filled up
  Fault protection limits tripped

## Slide 26: Anomaly: Data Storage and Fragmentation
Background Information
  Data storage and deletion lead to inevitable fragmentation of unused memory on data storage devices
  Level of fragmentation worsens with
    increasing number of write and delete operations
    memory space on the device filling up
  Problem exacerbated by inherent limits on the minimum size of data unit allowed to be stored
    Renders some of the smaller-size unused fragmented memory unusable

## Slide 27: Anomaly: Data Storage and Fragmentation
Background Information (Cont’d)
  Operating System typically issuing write and delete commands
  Storage device’s controller performing write and delete operations
  Operating System only aware of the overall amount of memory used, but not fragmented or unusable memory space

## Slide 28: Anomaly: Data Storage and Fragmentation
Cause of Anomaly
  87% of memory capacity of Solid-State Recorder (SSR) used prior to anomaly
  Operating System compared size of a data file to be stored against free memory in remaining 13% of memory capacity of SSR
  Data file size smaller than free space on SSR
  Operating System issued a write command to SSR

## Slide 29: Anomaly: Data Storage and Fragmentation
Cause of Anomaly (Cont’d)
  SSR’s controller scanned entire memory space on SSR and could not find large enough free fragmented memory to store requested data in
  Write command failed
  Some of subsequent commands to write other data also failed due to shortage of usable fragmented memory space
  In each case, SSR’s controller scanned memory space for each write request

## Slide 30: Anomaly: Data Storage and Fragmentation
Cause of Anomaly (Cont’d)
  Excessive time taken to repeatedly scan memory space for free memory made data waiting to be written back up in buffers

## Slide 31: Anomaly: Data Storage and Fragmentation
Project’s Solution
  Through flight rules, SSR not allowed to get more than 90% full

## Slide 32: Anomaly: Data Storage and Fragmentation
Observations
  Adverse effects of data fragmentation in space missions:
    Loss of full capacity of data storage device
    Further loss of storage capacity with increasing number of write and delete operations
    Loss of data due to write operation failures
    Latency issues in data handling
    Other potentially more-serious problems affecting spacecraft’s health and safety

## Slide 33: Anomaly: Data Storage and Fragmentation
Observations (Cont’d)
  Data storage at a premium in space missions
  Currently, no practical solution to avoiding loss of full capacity of data storage
  Practical solution to limiting or impeding further fragmentation of free space: Set an upper limit on level of memory to be utilized on data storage device
  Upper-limit memory solution adopted by project in response to anomaly

## Slide 34: Anomaly: Data Storage and Fragmentation
Observations (Cont’d)
  Project’s solution relying on flight rules
  Disadvantages of enforcing upper memory limit through flight rules
    Limit enforcement not precise – Requires continuous vigilance by mission operators in monitoring the memory usage level
    Limit enforcement not reliable – Depends on alertness, training, and consistency of flight operators
    Flight rules not subjected to IV&V – IV&V not usually engaged during software operation

## Slide 35: Anomaly: Data Storage and Fragmentation
Observations (Cont’d)
  Advantages of enforcing upper memory limit through software
    Limit monitoring and enforcement more precise and reliable
    Software development receiving IV&V analysis

## Slide 36: Anomaly: Data Storage and Fragmentation
IV&V Lessons
  Inevitability of data fragmentation
  Need to contain and manage data fragmentation by enforcing upper memory usage limit below full capacity of storage device
  Verify effectiveness of enforcing memory usage limit through software stress tests under realistic operational conditions:
    Accumulated number of write and delete operations undergone prior to start of test
    Size of data involved in write/delete operations

## Slide 37: Anomaly: Communication Protocols
Anomaly Description
  Downlink of a spacecraft’s housekeeping and science data resulted in generation of multiple error messages by FSW on several occasions

## Slide 38: Anomaly: Communication Protocols
Background Information
  Downlink of data utilized CFDP (CCSDS File Delivery Protocol), requiring handshake between spacecraft and ground
  Ground requesting downlink of a data file
  Upon receipt of data, ground sending an acknowledgement message to spacecraft
  Upon receipt of ground acknowledgement message,
    spacecraft marking downlinked data for deletion when its memory space needed
    spacecraft sending acknowledgement message to ground

## Slide 39: Anomaly: Communication Protocols
Background Information (Cont’d)
  Downlink transaction considered complete upon receipt of spacecraft acknowledgement message by ground
  Off-nominal case: Ground not receiving a final spacecraft acknowledgement message
    Ground re-sending own initial acknowledgement message to elicit spacecraft’s final acknowledgement message
      Re-sending message up to four times at regular intervals

## Slide 40: Anomaly: Communication Protocols
Background Information (Cont’d)
    If still no response from spacecraft,
      declare initial downlink a failure
      repeat downlink request all over
    Caveat: Lack of response from spacecraft not necessarily indicative of data downlink failure

## Slide 41: Anomaly: Communication Protocols
Cause of Anomaly
  Ground requested downlink of data
  Data downlinked
  Ground acknowledged downlink
  Spacecraft received ground’s acknowledgement
  Spacecraft marked downlinked file for deletion
  No acknowledgement received from spacecraft after repeated re-sending of ground’s initial acknowledgement

## Slide 42: Anomaly: Communication Protocols
Cause of Anomaly (Cont’d)
  Ground declared downlink a failure
  Ground re-initiated downlink request
  Data file requested for downlink already deleted on board spacecraft
  Error message issued by FSW for ground requesting downlink of a missing date file

## Slide 43: Anomaly: Communication Protocols
Project’s Solution
  Despite handshake fault, initial downlink found to be successful
  Downlinked data recovered from ground system
  For future downlinks, interval between re-sending ground’s acknowledgement (in response to off-nominal case) shortened
    In turn shortening time between initial and second downlink requests in off-nominal case
    Reducing likelihood of requested downlinked file having been deleted

## Slide 44: Anomaly: Communication Protocols
Observations
  Root cause of anomaly, i.e., reason for failure of receiving final acknowledgement from spacecraft, neither identified nor addressed in solution by project
  Many components in various segments and elements playing a role in downlink process
    Spacecraft and Ground segments
    Software and Hardware elements
    Human operators in MOC’s, SOC’s, ground stations

## Slide 45: Anomaly: Communication Protocols
Observations (Cont’d)
  Multiple sources of potential errors may lead to downlink anomalies

## Slide 46: Anomaly: Communication Protocols
IV&V Lessons
  Recognition of need for explicit elaborate requirements addressing every aspect of nominal and off-nominal data downlink
    Reference by project to downlink protocol standards as substitute to customized requirements not acceptable
      Standards may be incomplete and evolving
      Standards may not address peculiarities of a given mission

## Slide 47: Anomaly: Communication Protocols
IV&V Lessons (Cont’d)
  Expecting comprehensive set of tests to thoroughly verify data downlink requirements
    Burden on test scenarios to compensate for incomplete or missing requirements addressing both nominal and off-nominal conditions
    Injecting errors originating from numerous components of downlink process in tests

## Slide 48: Anomaly: Sharing Resources – CPU
Anomaly Description
  Command processing failed on a number of occasions on board a spacecraft in software processing instruments’ data

## Slide 49: Anomaly: Sharing Resources – CPU
Background Information
  Command processing and data compression both performed on the same computing processor
  Data compression a particularly computation-intensive operation
  Command processing, especially driven by a command script with a heavy load of commanding activities, also intensive in computing

## Slide 50: Anomaly: Sharing Resources – CPU
Cause of Anomaly
  Command processing failed while running simultaneously with data compression
  Both tasks sharing same CPU resources
  Data compression CPU-intensive
  Data compression given higher priority for CPU resources by FSW

## Slide 51: Anomaly: Sharing Resources – CPU
Project’s Solution
  Twofold solution
    FSW modified to allocate more CPU resources to command processing
    When command script carrying a especially heavy load of commanding activities, flight rules modified to disable data compression while command script executing

## Slide 52: Anomaly: Sharing Resources – CPU
Observations
  Sharing resources or commands may both lead to software faults
  Anomaly an example of two competing CPU-intensive tasks sharing limited CPU resources
  Missing performance requirements calling for adequate computing resources for simultaneously running tasks
  Inadequate performance testing of software under typical operational conditions

## Slide 53: Anomaly: Sharing Resources – CPU
IV&V Lessons
  Look for missing, incomplete, or incorrect performance requirements
    Performance requirements addressing both nominal and short-lived peak performance conditions
  Rigorously verify implementation of performance requirements through test analysis
    Expect comprehensive testing of software under nominal and off-nominal operational conditions to properly verify performance requirements

## Slide 54: Anomaly: Sharing Resources – CPU
IV&V Lessons (Cont’d)
  Determine restrictions on software operations due to performance considerations to be enforced through flight rules
    Even with adequate performance requirements and testing, may have to observe operational limits through flight rules
    Consult performance requirements, ICD’s, and test results

## Slide 55: OOAR Contact Information
Steve Husty – Lead
  stephen.husty@nasa.gov
Steve Pukansky
  stephen.m.pukansky@nasa.gov
Dan Painter
  joseph.d.painter@nasa.gov
Koorosh Mirfakhraie
  koorosh.mirfakhraie@nasa.gov