## Slide 1
Modeling the Image-Processing Behavior
of the NASA Voyager Mission with ASSL
Emil Vassev and Mike Hinchey

## Slide 2: AC & Space Exploration
Autonomic Computing (AC) – a solution to software complexity:
  Helps to implement self-adaptive and autonomic systems (ASs);
  Autonomic elements (AEs) – the architectural components of an autonomic system (AS)
  AC may handles complexity in spacecraft computer systems
  The new age of space exploration: NASA embarks in AC
  AC software helps to build the next generation of unmanned spacecraft;
  Autonomous Nano-Technology Swarm (ANTS) concept mission;
  Deep Space One (DS1) mission;

## Slide 3: Our Approach – Prototyping with ASSL
  AC-based ANTS-like and Voyager-like missions:
  Investigate hypotheses about the design and implementation of future Voyager-like missions based on the AC principles.
  Build prototype software models:
    help in the comparison of features and issues of the actual Voyager mission with hypothesized possible autonomic approaches;
    bring significant benefits to the development of future space-exploration systems.
  We experiment with ASSL (Autonomic System Specification Language) to realize these goals.

## Slide 4: Research Objectives
  Long-term objectives:
  model and implement with ASSL AS prototypes of future Voyager-like and ANTS-like missions;
  benchmark experiments - compare prototyped autonomic features and issues with the actual Voyager Mission;
  validate features in question and perform further investigations based on practical results under simulated conditions;
  First objective:
  specify with ASSL and generate a prototype model for the image-processing behavior observed in the Voyager mission.
  Event-driven behavior: Voyagers are able to detect space objects and take pictures of the same on-the-fly

## Slide 5: ASSL Specification Model
scalable specification model;
provides judicious selection and configuration of infrastructure elements and mechanisms for ASs;
decomposes an AS in two directions – 1) into levels of functional abstraction; 2) into functionally related sub-tiers;
presents the system from three different perspectives – 1) AS; 2) ASIP; 3) AE;
meets the AS builders needs;
flexible approach to specification.

## Slide 6: Specifying and Generating Prototypes with ASSL
  ASSL tiers - intended to specify different aspects of an AS, but only a few are needed to come up with a working model;
  an ASSL specification is built around self-management policies, which make that specification AC-driven;
  a complete specification:
    is validated with a built-in consistency checking tool;
    is used to automatically generate a functional prototype.
  generated prototypes: fully-operational multithreaded event-driven applications with embedded messaging;
ASSL Policy Specification
ASSELF_MANAGEMENT {
SELF_HEALING {
FLUENT inLosingSpacecraft {
INITIATED_BY { EVENTS.spaceCraftLost }
TERMINATED_BY { EVENTS.earthNotified }
}
MAPPING {
CONDITIONS { inLosingSpacecraft }
DO_ACTIONS { ACTIONS.notifyEarth }
}
}
}

## Slide 7: Autonomous Nano Technology Swarm (ANTS)
A novel approach to asteroid belt resource exploration;
Swarm of pico-class, low-power, and low-weight spacecraft:
  High autonomy - autonomous and adaptable agents;
  Exhibits self-organization emergent behavior;
Single spacecraft:
  Equipped with a solar sail;
  Onboard computation;
  Artificial intelligence techniques.

## Slide 8: ANTS Architecture
Workers - up to 80 percent of the swarm, bear instruments and gather data.
Rulers - coordinate data gathering through the use of rules.
Messengers - coordinate communications among the workers, rulers, and mission elements on Earth.

## Slide 9: ANTS Autonomic Properties
Self-configuration. ANTS must be fully reconfigurable to support concurrent exploration and examination of hundreds of asteroids.
Self-optimizing. ANTS must be able to improve its performance on the fly (group and individual).
    rulers;
    messengers;
    workers.
Self-healing. Any ANTS unit, teams, sub-swarms, and the entire swarm must be able to recover from both mistakes and failures.
Self-protecting. ANTS must be to anticipate and cure intrusions (for example, solar storms).

## Slide 10: Self-configuring
Goal: “On the fly” configuration of different teams of ANTS units,
to explore asteroids.
SELF_CONFIGURING – a self-management policy;
actions – a set of actions that could be undertaken by ANTS
events – a set of events that trigger and are triggered by the actions.
metrics – a metric that counts the number of detected asteroids.

## Slide 11: Self-Healing
Goal: Recover from failures, including those caused by damage due to a crash or any outside force.
proactive - heartbeat messages;
SELF_HEALING policy:
inCollision - the worker crashes;
inInstrumentBroken - the instrument is not operational anymore;
inHeartbeatNotification - initiated on a regular basis by a timed event to send the heartbeat message to the ruler;
checkANTInstrument (action) –instrument checking operation;
distanceToNearestObject (metric) - distance to the nearest object in space .

## Slide 12: Safety
Goal: ANTS safety objectives should present a level of safety that at least makes ANTS capable of operating under the following hazards:
  a collision with the other spacecraft units or asteroids;
  high-density magnetic fields;
  high radiation (due to a solar eruption);
  a high energy level (due to a solar eruption);
  a loss of communication among the ANTS AEs.
index 1
index 2
index 4
index 2
index 1
NASA Risk Index Determination

## Slide 13: Self-scheduling
Goal: self-scheduling mechanism in ANTS; some of the tasks could be time-constrained;
Modeling self-scheduling for ANTS:
  the most complex exercise;
  fault tolerance measures to both value and timing violations;
  capture the timing and schedulability requirements;
  model scheduling at group and individual level;
We specified self-scheduling as a distinct self-management policy

## Slide 14: Prospective ASSL Models for ANTS
Self-Optimizing:
  self-optimization for rulers - a process of learning;
  self-optimization for messengers - a process of positioning to balance the communications between the rulers;
  self-optimization for workers - a process of learning about the asteroids. This will allow workers to gain experience.
Self-Protecting:
  the self-protecting policy – should backs up the safety SLO at both individual and swarm levels;
  the self-protecting behavior of the team should be interrelated with the self-protecting behavior of the individual members.

## Slide 15: The Voyager Mission
  an extremely successful example for subsequent space missions;
  designed for exploration of the Solar System;
  continue to explore space: now on the special Voyager Interstellar Mission;
  Factors of success:
  rigorous spacecraft design and implementation;
  spacecraft hardware was designed to allow for enhanced remote control programming;
  autonomous behavior persists in the Voyager requirements;
  Voyager Spacecraft [The Planetary Society, “Space topics: Voyager – the story of the mission”]

## Slide 16: Image Processing Behavior
  1. The Voyager II spacecraft:
  uses its cameras to monitor space objects;
  takes a picture with its cameras;
  notifies Earth that an image transmission is about to start;
  applies color filters and sends the stream of pixels to Earth;
  notifies antennas on Earth for the end of each session.
  2. Antennas on Earth:
  are prompted to receive the image by special messages (one per applied filter);
  receive image pixels;
  are prompted to terminate the image sessions by special messages;
  send the collected images to the Voyager Mission base on Earth.
  3. The Voyager Mission base on Earth receives images from antennas.

## Slide 17: ASSL Model for Voyager
  we specified Voyager at the three main ASSL tiers – AS tier, ASIP tier, and AE tier;
  we specified the Voyager II spacecraft and the antennas on Earth as AEs that:
    follow their encoded autonomic behavior;
    exchange predefined ASSL messages over predefined ASSL communication channels.
  the Voyager mission autonomic behavior is specified at both AS and AE tiers as a self-management policy:
    the global autonomic behavior is determined by the specification of that policy at each AE and at the global AS tier.

## Slide 18
  a pure software solution – both spacecraft and antennas are implemented as interacting components in a Java application;
  has a multi-granular structure composed of instances (objects) of the specified tiers in the ASSL specification:
    a hierarchical composition where sub-tier instances are grouped around instances of major tiers.
Structure of the Generated Prototype

## Slide 19: Behavior of the Prototype
  log records show important state-transition operations ongoing in the system;
  these records help to trace and evaluate the behavior of the generated prototype model;
  Test results:
  The run-time behavior of the generated prototype model for the Voyager II mission strictly followed that specified with the ASSL IMAGE_PROCESSING self-management policy.

## Slide 20: Discussion and Future Work
  image-processing - programmed as an autonomic policy, but does not extend the original event-driven behavior observed in the Voyager Mission;
  the Voyager’s prototype abstracts most of the spacecraft components;
  the next prototype model:
    will specify the spacecraft’s radio, antenna, and two cameras as distinct managed elements - this will allow the evaluation of component behavior (via ASSL metrics and events);
    will extend the IMAGE_PROCESSING policy with other self-management features – two scenarios are planned: remote-assistance self-healing and on-board self-healing.

## Slide 21: Future Work
  further prototype development:
    detailed specification of the ANTS and Voyager spacecraft components;
    new autonomic features - self-healing, self-protecting, and self-adapting policies;
  construct an intelligent Voyager-like system able to react automatically to hazards in space by finding possible solutions and applying those on-board with no human interaction;
  a new ASSL model checking mechanism is currently under development – this will allow for automatic feature validation and discovery of design flaws;

## Slide 22: Benefits
  both the ASSL specifications and the generated prototypes can be extremely useful for the design and implementation of future ANTS-like andVoyager-like missions;
  the ability to compare features and issues with the actual mission and with hypothesized possible autonomic approaches gives significant benefit;
  we develop Voyager prototypes incrementally where each new prototype includes new autonomic features - this helps to evaluate the performance of each feature and gradually construct a model of a future Voyager-like system;
  this approach helps to discover eventual design flaws in both the original system and the prototype models;

## Slide 23
Thank you!
www.lero.ie