## Slide 1: Assurance Cases and Test Design Analysis
IV&V Workshop
September 11-13, 2012
Khalid Lateef Ph.D.

## Slide 2: Outline
Scope
Test Design challenges
Assurance cases
Example of test design IV&V for an automobile
Triggers – How to find the right triggers
Test Scenarios – All scenarios not created equal

## Slide 3: Scope and Acknowledgement
Scope
  Small part of the much larger risk assessment study
  Work initiated last year
  Validating Assurance cases approach against the Test analysis work already performed using traditional approach (CoM)
Acknowledgment
  IV&V supported Assurance case assessment (2011)
  Other NASA centers
  Non-NASA groups (SEI-CMU, Aerospace Corp, Adelard UK)
Notes:   CoM – Catalogue of Methods
  Non-NASA groups (SEI-CMU/Stephen Blanchette)
  Adelard - Robin Bloomfield and Peter Froome

## Slide 4: Test design
Test Results Verification
  Test design to wring out the bugs
  Was this effort successful?
Test design Validation – Nominal behaviors
  Relatively straightforward
  Not many issues discovered
Test Design Validation – Off nominal behaviors
  Takes more thought , What can go wrong? What shouldn’t it do? Off nominal behavior. Good number of issues
  What is “appropriately”? Off nominal behavior. Ripe for issues/ finding bugs
  Application the Safety Critical / Space Systems

## Slide 5: Off-nominal test design
DO-178B
Normal Range Test Cases:
  Boundary values on input variables
  Multiple iterations for time-related functions
  Transitions for state based software
Robustness Test Cases:
  Invalid values for variables
  System initialization under abnormal conditions
  Failure modes of incoming data
  Exceeded time frames
  Try to provoke illegal state transitions
  Arithmetic Overflow
  Loop counts
Notes: This slide contributed by Charlie Adkins

## Slide 6: Possible Inputs for the Test Design Analysis
Validated SW requirements
Test artifacts
  Test Plan
  Test procedures
  Test scripts
  Test Logs
Test artifacts associated with multiple builds
Con Ops, User manuals, Interface documents
Test validation scope based on PBRA and RBA

## Slide 7: Testing challenges-Space System
System Initialization
  Timing constraint
  Init Failure?
    Response from other systems or ground
Startup image management
  Auto switch to backup image?
    Appropriate bits commandable?
                (continued to next sheet)
Notes: Typical set. Not meant to be comprehensive list.

## Slide 8: Testing challenges-Space System (Contd.)
System Safety
  Fault Detection
    Fault levels (1, 2, or low level 3 fault)
  Fault response
    Autonomous/Manual Response enabled/inhibited
    Abort sequences (if applicable)
    Commands to enable / disable response, reset flags
    Swapping strings (IMOK monitoring)
  Preventative measures
    Arm/fire commands
    Command processing (FSW validates? Executes?)

## Slide 9: Assurance Case
What is an assurance case?
  Specialized instance of general case argumentation1
    Claim  Evidence (Build an argument using Evidence for a given claim)
  Claims can have sub-claims
Tools
  ASCE
  Excel
Notes: 2009 AIAA paper by Steve Blanchette

## Slide 10: Example: Test design analysis
Test design
  From the Test team
  Before the car is ready for full scale production or
  A batch of cars is ready to be shipped to the dealer / customer

## Slide 11: Claims
Claim#1: Radio/MP3 Player will work
Claim#2: Dome light will work
Claim#3: Test driver can drive the car along an intended course
  Sub-Claim#3.1: Car will start
  Sub-Claim#3.2: Car will stop

## Slide 12: Claim score based on safety, criticality
Score 1..5 each of the sub-claims
  Engine starts up (safely)
  Car can be stopped safely
  Airbag will deploy in case of an accident
Prioritization of claims based on score

## Slide 13: Engine Startup claim-evidence analysis
Startup scenario
  Key in ignition  Turn clockwise  xx seconds  Engine started
Claim: Engine will startup safely
  Evidence: Ignition control will not trigger if Shift selector is in drive (forward or reverse)
  Evidence: Ignition control will only trigger if the break pedal is in the specified position
  Evidence: Ignition control will not trigger if the engine already running
  Evidence: Ignition control will not trigger if the fuel pump or battery constraints are violated
Complexity of Test
Software testing is not about proving conclusively that the software is free from any defects, or even about discovering all the defects. Such a mission for a test team is truly impossible to achieve. Rex Black, Pragmatic Software Testing , John Wiley & Sons 2007

## Slide 14: Space System analysis
Claim Level 1 |  |  | Claim Level 2 |  |  | Claim Level 3 |  |  | Claim Level 4 |  |  | Claim Level 5 |  |  |  |  | Needed Evidence |  |  |  | Actual Evidence |  |  | 
Claim | Section | Score | Claim | Section | Score | Claim | Section | Score | Claim | Section | Score | Claim | Section | Score | Weight | Rationale | Requirement | Design | Implementation | Test | Requirement | Design | Implementation | Test

## Slide 15: Test scenario
Trigger -> Response
For each Claim, generate the list of triggers
For each trigger generate test scenarios
Test scenario
  The trigger for the requirement(s),
  Corresponding requirements and
  The type of data being processed / touched by the requirement(s)

## Slide 16: Trigger -> Response
Instrument
controller
HW
Test environment
User/Grnd Cmds
Telem data
HW Telem data
HW Cmd
Test Cmd / data
Telem data
Note 2: Generic diagram/table in the backup slides
Note 1: Annotations were added for the reference documents

## Slide 17: Space System Triggers / Responses
Triggers
  External commands / HW telem aka across the interfaces
  Internal (a relatively small number) to the system
Group the triggers (Single / multiple interfaces)
    User cmd impacting user interface only
    User cmd impacting User interface and hw interface
Responses
  Internal to the system
  To the external interfaces

## Slide 18: Test Design Validation Analysis & Evidence
  Test Scenario
    Test scenario trigger
    Test scenario step #
    Step description / behavior
  Reference info
    Source (document section number, Req tag number)
    Safety or criticality related to the test step
    Adverse conditions (if any)
  Evidence info
    Correlation to the test plan section
    Correlation to the test procedure (number, step)
    Correlation to the test script (code line number)
  Observations / Issues (if any)

## Slide 19: Test Design Issues verified
Incomplete Arm / fire Commands tests
Missing “Alternative” steps in the abort scenario tests
  Off nominal for abort-sequence
Inadequate fault flag responses tests
Incomplete Command parameter verification tests
Missing mode verification tests

## Slide 20: Two CSCIs of a Space system
~ 250 requirements each (Validated)
~ 45 ground commands each
Ground/SW interface
SW/HW interface
~60 test scripts each
  One with separate test design
  The second with high-level test procedure embedded in the test script (as comments)

## Slide 21: Summary
Assurance cases can help to
Develop comprehensive test scenarios
Systematic steps to uncover Off nominal conditions
  Off nominal conditions are the source of high severity issues with Test design and the system being tested
Identify and use system triggers as part of the test design analysis
Look for safety-critical test scenarios
Verify the test results
Review the issue resolutions for additional/new bugs

## Slide 22: Future Work
Using Assurance cases for
Analyzing test design
Test Coverage assessment
  Automated mapping
Independent testing

## Slide 23: Backup slides

## Slide 24: Verifying the test results
Test results Review
  Test logs
  Test terminal screen dumps
Test results show
  Commands executed
  Triggers identifiable
  Trigger occurred at the correct time
  System responses as expected
  Time stamps show if any deadlines violated