## Slide 1: A3 ROM Cost Assessment
27 June 2017

## Slide 2: A3 ROM Cost Assessment
Statement of Work Sub‐Task 6 – A3 Full Scale Test ROM Estimate Assessment
BWXT activities include:
  Evaluate equipment/system needs and quantities from the structures, systems, and components described in the A3 test stand gap assessment document NASS‐ES‐100889
  Provide the quantities of mechanical, electrical, and I&C hardware required to meet the requirements of the conceptual A3 test stand design
  Provide input to NASA for creation of a ROM cost estimate of the equipment
  Estimate engineering and licensing costs for A3 ground test
Notes: Is our equip list one of several inputs?
We need to understand the baseline in more detail
Made progress under this SOW to set nuclear expectations for design considerations

## Slide 3: A3 ROM Cost Assessment
Process to develop equipment list –
  Review NASS‐ES‐100889 and develop a high level process flow diagram for each system identified. No design work performed
  Estimate operating philosophy
  Identify equipment required
  Estimate layout to determine feet of pipe/duct required
  Perform preliminary sizing for equipment identified
  Develop equipment list for each system
  Estimate which systems will be safety related
  Perform similar tasks for electrical and I&C systems/equipment

## Slide 4: A3 Full Scale ROM Assessment
Existing NASA ground test concept divided into 22 systems /subsystems
Additional 21 systems were identified to address identified gaps
Develop functions and concepts for the additional systems
Evaluate equipment types and sizes, approximate instrument and electrical needs, estimate safety related functions and equipment
NTP-GTF Systems Breakdown
(BWXT: NASS-ES-100889)

## Slide 5: System Example

## Slide 6: Design Aspects Influencing ROM
Baseline design based on April 20 meeting:

## Slide 7: Design Aspects Influencing ROM
Design Differences – Nuclear Cooling / Confinement Influence
  Spray/Diffuser Cooling – Once through De-ionized (DI) water
  Use of Higher Pressure Industrial Water (HPIW) to cool diffuser and condense the exhaust
  Gas removal from exhaust storage
Work completed that applies to current design
  LH2 and LO2 supply
  Cooling required for fuel quenching
  Test Cell
  Effluent Gas Handling

## Slide 8: ROM BOM Approach
Focus on systems needed to license the design with the US Nuclear Regulatory Commission
Consider events that will influence the design
  Results in additional systems and/or requirements
  Decay Heat Removal
  Emergency Core Cooling
  Requirements on LH2, LO2, Cooling Water supply
  Shielding
  Radiation Monitoring
  Radwaste systems
  Severe Accident Mitigation – Core relocation

## Slide 9: Event Considerations Influencing ROM
Normal Operation:
  Power Operation
    Assume No Fuel Leakage, No Radiation Outside of Shield Test Cell
    Assume Partial Fuel Leakage, or Shine through Diffuser
  Startup Conditions
    No Fuel Leakage (New Fuel)
  Shutdown Conditions
    No Fuel Leakage (Spent Fuel)
    Shutdown Conditions (Assume Partial Fuel Leakage, Shine where fuel relocation has occurred)

## Slide 10: Event Considerations Influencing ROM
Potential Maximum Hypothetical Events:
  Pipe Break/Loss of Hydrogen Coolant At Power Conditions
  Loss of Diffuser Active Cooling Resulting in Fire
Severe Accident:
  Complete Relocation (One Piece), Core Critical
In slides below:
  Red reflects a difference with the current concepts as we understand.
  Black is expected.
  Figures based on new concept for discussion. Where an item was previously noted, it was not included again to help simplify

## Slide 11: Event Considerations Influencing ROM
Normal Power Operation
  Power Operation, Assume No Fuel Leakage, No Radiation Outside of Shield Test Cell
    H2/Reactor Coolant
      Core Heat Removal (Potentially Safety Related)
    Reactor
    Digital Control
    Exhaust Capture
    Auxiliary Support Systems
      Process and Effluent Radiation Monitoring. (Potentially Non-safety Related)
    Electrical Systems
    Security Control
Notes: Safety-Related (NRC Glossary): In the regulatory arena, this term applies to systems, structures, components, procedures, and controls (of a facility or process) that are relied upon to remain functional during and following design-basis events. Their functionality ensures that key regulatory criteria, such as levels of radioactivity released, are met. Examples of safety-related functions include shutting down a nuclear reactor and maintaining it in a safe-shutdown condition.
Basic component. (10 CFR Part 21, Section 21.3, Definitions)
(1)(i) When applied to nuclear power plants licensed under 10 CFR part 50 or part 52 of this chapter, basic component means a structure, system, or component, or part thereof that affects its safety function necessary to assure:
(A) The integrity of the reactor coolant pressure boundary;
(B) The capability to shut down the reactor and maintain it in a safe shutdown condition; or
(C) The capability to prevent or mitigate the consequences of accidents which could result in potential offsite exposures comparable to those referred to in § 50.34(a)(1), § 50.67(b)(2), or § 100.11 of this chapter, as applicable.
(ii) Basic components are items designed and manufactured under a quality assurance program complying with appendix B to part 50 of this chapter, or commercial grade items which have successfully completed the dedication process.
(2) When applied to standard design certifications under subpart C of part 52 of this chapter and standard design approvals under part 52 of this chapter, basic component means the design or procurement information approved or to be approved within the scope of the design certification or approval for a structure, system, or component, or part thereof, that affects its safety function necessary to assure:
(i) The integrity of the reactor coolant pressure boundary;
(ii) The capability to shut down the reactor and maintain it in a safe shutdown condition; or
(iii) The capability to prevent or mitigate the consequences of accidents which could result in potential offsite exposures comparable to those referred to in §§ 50.34(a)(1), 50.67(b)(2), or 100.11 of this chapter, as applicable.
(3) When applied to other facilities and other activities licensed under 10 CFR parts 30, 40, 50 (other than nuclear power plants), 60, 61, 63, 70, 71, or 72 of this chapter, basic component means a structure, system, or component, or part thereof, that affects their safety function, that is directly procured by the licensee of a facility or activity subject to the regulations in this part and in which a defect or failure to comply with any applicable regulation in this chapter, order, or license issued by the Commission could create a substantial safety hazard.
(4) In all cases, basic component includes safety-related design, analysis, inspection, testing, fabrication, replacement of parts, or consulting services that are associated with the component hardware, design certification, design approval, or information in support of an early site permit application under part 52 of this chapter, whether these services are performed by the component supplier or others.

## Slide 12: Event Considerations Influencing ROM
  Related to Figure Provided:
Core Heat
Removal
Process &
Effluent Rad.
Monitoring

## Slide 13: Event Considerations Influencing ROM
Normal Power Operation (Cont.)
  Power Operation, Assume some Radionuclide transport from Fuel, or Shine through Diffuser
    H2/Reactor Coolant
      Core Heat Removal (Potentially Safety Related)
    Reactor
    Digital Control
    Exhaust Capture
    Auxiliary Support Systems
      Radiation Monitoring. (Potentially Non-safety Related)
      Dedicated Rad Systems (Drains, HVAC)
    Radioactive Waste Management (Potentially Non-safety Related)
    Electrical Systems
    Security Control
    Shielding
      Assumed 1% Leakage of Fission Products

## Slide 14: Event Considerations Influencing ROM
  Related to Figure Provided:
Shielding (Esp.
For Neutrons/
Gammas)
Dedicated Rad Systems Not Shown (Drains/HVAC), radiologically controlled area unclear.
Radwaste Management (Not shown)

## Slide 15: Event Considerations Influencing ROM
Normal Power Operation (Cont.)
  Startup Conditions, No Fuel Leakage:
    Air/Fuel Transfer (New Fuel)
      Fuel Handling & Storage
    N2/Inert
    H2/Reactor Coolant
    Reactor
    Digital Control
    Exhaust Capture
    Auxiliary Support Systems
      Process and Effluent Radiation Monitoring. (Potentially Non-safety Related)
    Electrical Systems
    Security Control

## Slide 16: Event Considerations Influencing ROM
Normal Power Operation (Cont.)
  Shutdown Conditions, No Fuel Leakage:
    Air/Fuel Transfer (Spent Fuel)
      Fuel Handling & Storage (Potentially Safety Related and Non safety related, Augmented Quality)
    N2/Inert
    H2/Reactor Coolant
      Transition to Decay Heat Removal (Potentially Safety Related)
    Reactor
    Digital Control
    Exhaust Capture
    Auxiliary Support Systems
      Process and Effluent Radiation Monitoring. (Potentially Non-safety Related)
    Electrical Systems
    Security Control
    Shielding

## Slide 17: Event Considerations Influencing ROM
  Related to Figure Provided:
Spent Fuel Handling and Storage Not Shown
Intended Configuration for Decay Heat Removal Unclear

## Slide 18: Event Considerations Influencing ROM
Normal Power Operation (Cont.)
  Shutdown Conditions, Assume Partial Fuel Leakage, Shine where fuel relocation has occurred:
    Air/Fuel Transfer (Spent Fuel)
      Fuel Handling & Storage (Potentially Safety Related and Non safety related, Augmented Quality)
    N2/Inert
    H2/Reactor Coolant
    Reactor
    Digital Control
    Exhaust Capture
    Radioactive Waste Management (Potentially Non-safety Related)
    Auxiliary Support Systems
      Process and Effluent Radiation Monitoring. (Potentially Non-safety Related)
      Dedicated Rad Systems (Drains, HVAC)
    Electrical Systems
    Security Control
    Shielding

## Slide 19: Event Considerations Influencing ROM
Maximum Hypothetical Events
  Pipe Break/Loss of Hydrogen Coolant From At Power Condition
    H2/Reactor Coolant
      Pressurized Test Cell
      Engineering Safeguards - Emergency Hydrogen Core Cooling (Potentially Safety Related)
      Engineering Safeguards - Transition to Decay Heat Removal (Potentially Safety Related)
    Reactor
      Reactor trip using Control Drums (Potentially Safety Related)
    Digital Control
      Facility Protection Layer (Potentially Safety Related)
    Exhaust Capture (Portions potentially Safety-Related)
    Auxiliary Support Systems
      Radiation Monitoring. (Potentially Non-safety Related)
      Cooling Water (Potentially Safety Related)
      Spray Water (Potentially Safety Related)

## Slide 20: Event Considerations Influencing ROM
Maximum Hypothetical Events (Cont.)
  Pipe Break/Loss of Hydrogen Coolant From At Power Condition (Cont.)
    Radioactive Waste Management (Non-safety, Augmented Quality)
    Electrical Systems
      Divisional support of electrical systems. (Potentially Safety Related)
    Security Control
    Shielding
      Assumed Partial Core Relocation Due to Structural Degradation
    Structural Support (Potentially Safety Related)

## Slide 21: Event Considerations Influencing ROM
  Related to Figure Provided:
No Configuration for ECC Present
Potentially Safety Related
Completely Passive System for normal operation with turbo pumps, as compared to safety case uncertain.
Test Cell Pressurization
Particulate Transfer Handling Unclear
Must assure redundancy, diversity and separation for those items deemed safety related.
Safety Related
Cooling Function?
Notes: Single Failure (10 CFR 50 Appendix A):
Single failure. A single failure means an occurrence which results in the loss of capability of a component to perform its intended safety functions. Multiple failures resulting from a single occurrence are considered to be a single failure. Fluid and electric systems are considered to be designed against an assumed single failure if neither (1) a single failure of any active component (assuming passive components function properly) nor (2) a single failure of a passive component (assuming active components function properly), results in a loss of the capability of the system to perform its safety functions2.
2 - Single failures of passive components in electric systems should be assumed in designing against a single failure. The conditions under which a single failure of a passive component in a fluid system should be considered in designing the system against a single failure are under development.

## Slide 22: Event Considerations Influencing ROM
Maximum Hypothetical Events
  Loss of Diffuser Active Cooling Resulting in Fire
    H2/Reactor Coolant
    Reactor
      Reactor trip using Control Drums (Potentially Safety Related)
    Digital Control
      Facility Protection Layer (Potentially Safety Related)
    Exhaust Capture
    Auxiliary Support Systems
      Cooling Water (Potentially Safety Related)
      Spray Water (Potentially Safety Related)
      Radiation Monitoring. (Potentially Non-safety Related)

## Slide 23: Event Considerations Influencing ROM
Maximum Hypothetical Events
  Loss of Diffuser Active Cooling Resulting in Fire
    Radioactive Waste Management (Potentially Non-safety, Augmented Quality)
    Electrical Systems
      Divisional support of electrical systems.
    Security Control
    Shielding
      Assumed Partial Core Relocation Due to Structural Degradation.
    Structural Support (Potentially Safety Related)

## Slide 24: Event Considerations Influencing ROM
  Related to Figure Provided:
What assures mission of cooling diffuser? Must assure redundancy, diversity and separation.

## Slide 25: Event Considerations Influencing ROM
Severe Accident
  Complete Core Relocation (One Piece), Core Critical
    Digital Control
    Exhaust Capture
      Missile Protection
      Water Management to avoid steam explosion.
    Auxiliary Support Systems
      Radiation Monitoring. (Potentially Non-safety Related)
      Dedicated Rad Systems (Drains, HVAC)
    Radioactive Waste Management (Potentially Non-safety, Augmented Quality)
    Electrical Systems
    Security Control
    Shielding
    Robust External Structure

## Slide 26: Event Considerations Influencing ROM
  Related to Figure Provided:
No Debris Trap/Water Management shown. What mitigates steam explosion in the event of complete core relocation?

## Slide 27: Next Steps
Design and Licensing processes are developed together
BWXT has the expertise to both complete and integrate processes
Design experience with other nuclear designs and NASA concepts gained through the ROM BOM process
BWXT has broad design and licensing experience
  13 NRC issued licenses to fabricate, process, utilize and store nuclear materials
  Provided design and licensing support to nuclear utilities for 34 nuclear power plants
  NRC pre-application work for MIPS non power reactor
  Currently fabricates the fuel assemblies for HFIR, ATR, MITRR
  Past specialty work efforts on SNTP and JIMO projects