| PAYLOAD NAME: |  |
| --- | --- |
| NAME OF INDIVIDUAL COMPLETING CHECKLIST: |  | DATE: |  |
| NOTE: Prior to completion of this checklist, contact the applicable program office to request access to referenced NASA documents and drawings. Check Yes, No, or Not Applicable (N/A) for each item. Unless otherwise noted, each item includes all aspects of ground handling as well as flight operations. To elaborate on any checklist item, enter comments on page 3. |

|  |  |  |  | Yes | No | N/A |
| --- | --- | --- | --- | --- | --- | --- |
| I. TEST EQUIPMENT STRUCTURAL DESIGN REQUIREMENTS |  |  |  |
| 1. Structural integrity to aircraft crash loads of all equipment to be flown on board NASA JSC AOD heavy aircraft has been verified [via accepted method(s)], documented accordingly, and approved by AOD Engineering. Structural analysis is to use aircraft specific installation/attachment/load capacity criteria. |  |  |  |
| II. AIRCRAFT LOADING |  |  |  |
| 1. All hardware is designed for aircraft installation with enough clearance to avoid the risk of damaging aircraft structure. |  |  |  |
| 2. All hardware is designed to be compatible with standard materials handling equipment and procedures. |  |  |  |
| 3. All hardware is designed to be manually handled; handles, and/or lifting bars, points, etc. are to be rated at less than 50 pounds per person. |  |  |  |
| 4. Hardware does not exceed aircraft weight limits. |  |  |  |
| III. PRESSURE/VACUUM SYSTEM REQUIREMENTS |  |  |  |
| 1. All pressure/vacuum systems proposed for flight and/or ground use comply with JPR 1710.13, Design, Inspection, and Certification of Pressure Vessels and Pressurized Systems. |  |  |  |
| 2. If required, an OCCP (Operation and Configuration Control Plan) has been issued by the JSC Materials and Process Branch, or equivalent. |  |  |  |
| IV. ELECTRICAL |  |  |  |
| 1. All electrical wiring and interconnect cabling is fabricated and installed in accordance with JPR 1700.1, JSC Safety and Health Handbook, the National Electrical Code (NEC), and/or SAE AS 50881, Wiring Aerospace Vehicle, as applicable, per AOD Engineering. |  |  |  |
| 2. Customers use wire sizes and circuit breakers in accordance with the NEC or SAE AS 50881. Wire types are in accordance with NASA drawing 8593003, Wire, Electric, Interconnection, and Hookup. |  |  |  |
| 3. The payload has emergency shutdown capabilities to completely deenergize the entire payload including back-up power systems such as batteries or uninterruptible power supplies. |  |  |  |
| 4. In the event of electrical power loss (expected or unexpected), all payloads fail to a safe configuration. |  |  |  |
| 5. All electrical aircraft interface cables have a descriptive tag secured to each end with information to include the payload name and cable number. |  |  |  |
| 6. Total electrical power loads have been calculated and electrical power requirements are coordinated with the appropriate aircraft program office. |  |  |  |
| 7. All cables within the payload are adequately restrained and clamped. |  |  |  |
| 8. Electrical insulation is protected against abrasion and chaffing. |  |  |  |
| 9. Any exposed metal surfaces are adequately grounded to prevent electrical shock. |  |  |  |
| 10. The payload is self-protected with an incorporated circuit breaker or other current-limiting device. |  |  |  |
| 11. All batteries used are approved by the appropriate aircraft program office. |  |  |  |
|  |  |  |  | Yes | No | N/A |
| V. OVERBOARD VENT |  |  |  |
| 1. The chemical composition and quantity of the vented gas is entirely known and documented, along with hazards, mitigation, and potential interaction. |  |  |  |
| 2. The equipment is designed with interface to aircraft vent manifolds. |  |  |  |
| VI. RADIATION SAFETY |  |  |  |
| 1. Design and use of laser systems, radioactive materials, radio frequency, etc. complies with JPR 1700.1. All applicable forms have been submitted and approved by the JSC Radiation Safety Office and other governing bodies, as necessary. |  |  |  |
| VII. EMERGENCY PROCEDURES |  |  |  |
| 1. Emergency procedures are provided to the appropriate aircraft program office in checklist format and aircrew have been trained as to how to fail-safe the payload and NASA aircrew are able to safely and efficiently initiate emergency procedures to fail-safe a payload in the event of an emergency. |  |  |  |
| VIII. HAZARDOUS MATERIALS |  |  |  |
| 1. Necessary provisions for appropriate use of hazardous materials in-flight and on the ground are identified and documented. |  |  |  |
| 2. A current Safety Data Sheet (SDS) is supplied to the appropriate aircraft program office for each hazardous material. PPE (Personal Protective Equipment) is being provided by the payload team and will be used as detailed in the SDS. Hazardous materials will be stored as per the SDS. |  |  |  |
| IX. MISCELLANEOUS |  |
| 1. All hard and sharp edges that could conceivably be accessed by voluntary or involuntary operations are guarded. |  |  |  |
| 2. The payload can tolerate flight environments. |  |  |  |
| 3. Any frangible items, glass, CRTs (Cathode Ray Tubes), gauges, windows, or any other object that is susceptible to shattering is entirely contained. |  |  |  |
| 4. Payload pump designs are coordinated with the appropriate aircraft program office. |  |  |  |
| 5. Camcorders, cameras, tape recorders, etc. are brought on board the aircraft, they are securely stowed during takeoff and landing, and always under control during flight. |  |  |  |
| 6. Fluids approved for flight are contained in a system that is structurally sound to withstand g-loads specified and any inadvertent contact loads. |  |  |  |
| 7. Hardware maintains a touch temperature of no greater than 122(F (50(C). Guards or other protection measures are employed for payload hardware where the touch temperatures are greater than 122(F (50(C). |  |  |  |
| 8. Noise levels do not to exceed established limits for all operations. |  |  |  |
| 9. Non-United States citizen participation has been coordinated with the appropriate aircraft program office. |  |  |  |
| 10. Proper security protocols are in place for ground handling, in flight operation, and data processing (also considering aircraft emergency divert locations). |  |  |  |
| X. RISK ANALYSIS |
| 1. AOD Form 195, JSC Aircraft Operations Risk Analysis, has been completed for each payload. |  |  |  |

XI. COMMENTS