## Slide 1: Risk-based SMA for cubesats
Jesse Leitner, Chief SMA Engineer
NASA GSFC
December, 2016
Notes: What do our colors really mean?
  Yellow (Warning)
    Management awareness/attention needed
    Items usually get discussed at Division/Directorate meetings
  Red (Critical)
    Impact is significant and management awareness/attention needed
    Items usually get discussed at Directorate/Center meetings

## Slide 2: Outline
  Cubesat philosophy and constraints
  Risk Classification for cubesats
  Mission Success activities to reduce defects
  Risk-based SMA
  Scaling of efforts for cubesats
  Building a cubesat mission success strategy from ground up
  Cubesat lifetime
  Cubesat as an inherited item

## Slide 3: Cubesat philosophy
Understand the constraints
  Size (space limitations)
  Proximity of elements
  Cost and schedule resources
Recognize the limited reliability history
  Cubesat level – few developments using “high reliability” approach
  Cubesat components – very little reliability basis
Develop new approach for establishing reliability
  Will require time to accumulate on-orbit data for system reliability
  Apply proven component-level accelerated testing approaches
    Ensure accelerated testing is validated against actual product reliability experiences (based on product failures in a relevant environment) - be wary of “non-TAYF” lifetesting
    Overly conservative approach will be a showstopper
  Explore means for accelerated testing at system-level
  This is a ripe environment for model-based systems engineering and model-based mission assurance
Determine efforts that provide the best bang for the buck
  Will not be able to afford typical minimum mission success activities for larger spacecraft
At time of launch – be sure cubesat was thoroughly tested in environment and functions properly
  Open questions (unresolved anomalies) and limited system testing time are reliability threats
When possible, target constellation-level reliability
  Never at the expense of the debris environment or threats to people or property on the ground
How do we best apply the available programmatic risk commodity and cost and schedule resources to make technical risk as low as possible?

## Slide 4: What is risk classification?
Establishment of the level of risk tolerance from the stakeholder, with some independence from the cost
  Cost is covered through NPR 7120.5 Categories
If we were to try to quantify the risk classification, it would be based on a ratio of programmatic risk tolerance to technical risk tolerance
  For Class A, we take on enormous levels of programmatic risk in order to make technical risk as close to 0 as possible. The assumption is that there are many options for trades and the fact is that there must be tolerance for overruns.
  For Class D, there will be minimal tolerance for overruns and a greater need to be competitive, so there is a much smaller programmatic risk “commodity” to bring to the table
The reality is that the differences between different classifications are more psychological (individual thoughts) and cultural (longstanding team beliefs and practices) than quantitative
There is one technical requirement from HQ associated with risk classification: single point failures on Class A missions require waiver

## Slide 5: Risk Classification
NPR 7120.5 Class C: Moderate risk posture
  Represents an instrument or spacecraft whose loss would result in a loss or delay of some key national science objectives.
  Examples: LRO, MMS, TESS, and ICON
NPR 7120.5 Class D: Cost/schedule are equal or greater considerations compared to mission success risks
  Allowable technical risk is medium by design (may be dominated by yellow risks).
  Many credible mission failure mechanisms may exist. A failure to meet Level 1 requirements prior to minimum lifetime would be treated as a mishap.
  Examples: LADEE, IRIS, NICER, and DSCOVR
NPR 7120.8 “Class” – Allowable technical risk is high
  Some level of failure at the project level is expected; but at a higher level (e.g., program level), there would normally be an acceptable failure rate of individual projects, such as 15%.
  Life expectancy is generally very short, although instances of opportunities in space with longer desired lifetimes are appearing.
  Failure of an individual project prior to mission lifetime is considered as an accepted risk and would not constitute a mishap. (Example: ISS-CREAM)
“Do No Harm” Projects – If not governed by NPR 7120.5 or 7120.8, we classify these as “Do No Harm”, unless another requirements document is specified
  Allowable technical risk is very high.
  There are no requirements to last any amount of time, only a requirement not to harm the host platform (ISS, host spacecraft, etc.).
  No mishap would be declared if the payload doesn’t function. (Note: Some payloads that may be self-described as Class D actually belong in this category.) (Example: CATS, RRM)

## Slide 6: Defects vs Mission Success
Risk can be characterized by number of defects that affect performance or reliability
and the impact of each. Defects are generally of design or workmanship.
Note: A thorough environmental test program will ensure most risks are programmatic (cost/schedule) until very late, when time and money run out.
Random vibe
S/W engineering and QA
Number of Residual Design Defects
Mission Success Activities
GOLD rules
Internal review
Independent review 1
Independent review 2
4 T cycles
EMI self-compatibility
Sine sweep
Acoustic
Strength testing/analysis
EMC
Full EMI/EMC
S/W engineering and QA
FPGA requirements
Detailed design FMEA
Full PRA
Number of Residual Workmanship Defects
Mission Success Activities
1st tier QA
2nd tier QA
3rd tier QA
4 T cycles
4 more T cycles
Random vibe
Sine burst
EMI self-compatibility
Full EMI/EMC
Fastener integrity
GIDEP broad assessments
QPL parts
Workmanship requirements
Prohibited materials
EM work
Functional FMEA

## Slide 7: Defects vs Mission Success as a function of risk classification
Generally-representative example, prioritization may vary by mission attributes or personal preference or experience.
Mission Success Activities
Closed Loop GIDEP and alerts
Workmanship-trained techs
Number of Residual Defects
GOLD rules
EMC
Class D
Class C
Class B
Class A
DNH 7120.8
Graybeard Internal review
Independent review 1
Independent review 2
Close-out inspection
2nd tier QA
3rd tier QA
4 T
cycles
4 more T cycles
Random vibe
150 failure free hours
Sine sweep
Acoustic
EMI self-compatibility
S/W engineering
FPGA requirements
Fastener integrity
Design FMEA/FTA
Full PRA
QPL parts
Prohibited materials
EM work
Functional FMEA
GIDEP internal disposition
Full EMI/EMC
Workmanship requirements
500 operating hours
500 more operating hours

## Slide 8: Programmatic risk of reduced efforts
Cost to remove a single defect
Time at which defect is caught
The more layers that are removed, the later defects are likely to be caught (if they are caught), the more work that has to be “undone”, the more testing that has to be redone, and the more likely the project is to suffer severe programmatic impact and/or to fly with added residual risk.
Launch
date
Mission
Cost +
Removing layers results in some defects not being caught,
and some being caught later

## Slide 9: What is Risk-Based SMA?
The process of applying limited resources to maximize the chance for safety & mission success by focusing on mitigating specific risks that are applicable to the project vs. simply enforcing a set of requirements because they have always worked

## Slide 10: Risk-based SMA
Risk-informed framework
Risk-informed requirements generation
Risk-informed decisions
Risk-informed review and audit

## Slide 11: Attributes of Risk-Based SMA
Note: Always determine the cause before making repeated attempts
to produce a product after failures or nonconformances
Upfront assessment of reliability and risk, e.g. tall poles, to prioritize how resources and requirements will be applied
Early discussions with developer on their approach for ensuring mission success (e.g., use of high-quality parts for critical items and lower grade parts where design is fault-tolerant) and responsiveness to feedback
Judicious application of requirements based on learning from previous projects and the results from the reliability/risk assessment, and the operating environment (Lessons Learned – multiple sources, Cross-cutting risk assessments etc)
Careful consideration of the approach recommended by the developer
Characterization of risk for nonconforming items to determine suitability for use – project makes determination whether to accept, not accept, or mitigate risks based on consideration of all risks
Continuous review of requirements for suitability based on current processes, technologies, and recent experiences
Consideration of the risk of implementing a requirement and the risk of not implementing the requirement.
Notes: Requirements will be assigned based on the specific project attributes, but even after they are assigned, there is always an opportunity to question them.

## Slide 12: Scaling of efforts for cubesats
In general, mission success activities for cubesats do not scale down linearly as compared to larger missions
  Environmental test
    Elements of “religion” (number of thermal cycles, sine vs random, etc) do not scale down
    Time to reach thermal equilibrium does scale down
  Inspection
    Overhead of performing inspection at various points remains
    Volume of inspection does scale down
  Operating time
    Operating time to ensure system-level design and workmanship issues are exposed does not scale down
  Qualification of new elements does not scale down

## Slide 13: Building an SMA approach from the ground up
Mission Success Tiers: For a given application, arrange mission success activities from low ratio of programmatic risk to technical risk and low ratio of cost-and-schedule resources to technical risk to high ratio of programmatic risk to technical risk and high ratio of cost-and-schedule resources to technical risk
Build mission success activity profile based on risk tolerance (risk classification): Recommend graded approach of applying activities starting from low ratios, working towards high, to build the lowest achievable risk posture holistically, within resource constraints
Expected lifetime: Apply processes and analyses that address lifetime concerns:
  Limited life items
  Expendables
  Qualification period duration or accelerated life (or other reliability basis)

## Slide 14: Sample from Tables (Mission Success lower tiers)
2A: Medium Ratio of Programmatic Risk to Technical Risk Protoflight vibe RS testing | 2B: Medium Ratio of Programmatic Resources to Technical Risk 3-6 TVAC cycles (after 2 earlier) Level 3 EEE parts 1000 or more hours of operation Select mandatory inspection points Use of formal WOA system Select engineering units for high risk/new items Focused engineering peer review Fault-tolerant design using FMECA, FTA, and/or critical items analysis as a basis Design for manufacturability FPGA peer review Observatory level qualification Self-performed software assurance GIDEP self-review GOLD rules as guidance Radiation qualification by similarity
3A: Low Ratio of Programmatic Risk to Technical Risk First two TVAC cycles, minimum 50 hours Last 150 hours of failure free operation Vibe at 1.05 flight levels EMI self-compatibility Radiation-tolerant design | 3B: Low Ratio of Programmatic Resources to Technical Risk First four thermal cycles EEE part derating Parts stress analysis Random vibe First 500 hours of operation Close-out inspection Early holistic risk assessment “iphone” photography informal independent SME review (graybeard mentoring) spare printed circuit board or coupon for future DPA

## Slide 15: Sample from Tables (Risk Tolerance)
 | 7120.5 Class C | 7120.5 Class D | 7120.8 | Do No Harm
Stakeholder perspective | An instrument or spacecraft whose loss would result in a loss or delay of some key national science objectives. New technologies may be employed that may not be fully compatible with some traditional requirements, requiring alternative approaches for ensuring mission success. | Cost and schedule are of equal or greater consideration compared to mission success risks. Allowable technical risk is medium by design (may be dominated by yellow risks). Many credible mission failure mechanisms may exist. New technologies may be employed that may not be fully compatible with some traditional requirements. | Acceptable technical risk is high. Some level of failure at the project level is expected but at a higher level (program level), there would normally be an acceptable failure rate of individual missions (such as 85% mission success rate over some time period). Premature failure of an individual mission is considered as an accepted risk, and not a mishap. | Acceptable technical risk is very high. There are no requirements to last any amount of time, only not to harm the host platform (ISS, host spacecraft, etc.). No mishap would be declared if the mission doesn’t perform as planned. Such missions may be considered to be an “on-orbit environmental test”.
Key emphasis | Robust testing and consideration of fault tolerance in the mission architecture and hardware designs | Thorough testing and some consideration of fault tolerance | “Program level” fault tolerance (some failures expected) | Protecting the host, learning from anomalies and failures
Tier selection | 2A, 2B, 3A, 3B, select levels from 1A, 1B | 3A, 3B, and select 2A and 2B elements | 3A and 3B | Select 3A and 3B elements

## Slide 16: Expected lifetime
 | < 3 months | 3-months-1 year | 1-5 years | > 5 years
Main attributes | Min. 100 hrs system-level testing time. No additional EEE part or component screening or qualification (acceptance only) – does it function at launch | Min. 200 hrs system-level testing time. Selective part/component screening and qualification (beyond COTS) – thorough environmental test | Min. 500 hrs system-level testing time. Thorough part and component screening and qualification, thorough environmental test | Min. 1000 hrs system-level testing time. Complete part and component screening and qualification, testing consistent with large spacecraft
Limited life (LL) items, expendables | Sizing expendables is the primary consideration | Increased analysis or margins for expendables plus analysis or test for selected LL items | Increased analysis and margins for expendables plus analysis and test for most LL items | Increased analysis and margins for expendables plus analysis and test for all LL items

## Slide 17: Other Processes
Materials: NASA-STD-6016 with discretion
Workmanship: NASA trained technicians
ESD – aligned with sensitivity, not necessarily risk-tolerance
Interface FMEA to protect the host platform and the environment
Launch/range safety
  Tailored NASA-STD-8719.24
  LSP-Req-317.01 (for LSP hosted cubesats)
Debris requirements from NPR 8715.6, NASA-STD-8719.14

## Slide 18: Inherited Items Process
Baselined in GPR 8730.5: SMA acceptance of inherited and build-to-print hardware
Centrally handled for all projects to ensure that process is implemented uniformly and that prior analyses are used to the greatest extent
Folds in the more traditional heritage reviews to this process

## Slide 19: Example Standard Components
Star Trackers
Gyros/IMUs
Reaction Wheel Assemblies
Magnetometers
Torquer bars
Battery Relays
High performance stepper motors and actuators
Piezoelectric motors

## Slide 20: “Traditional” GSFC SMA practices
Strongly requirements-based
Commercial practices only by exception
Previously-developed and build-to-print items required to meet all requirements or work through standard MRB process
Treatment of each item as if it is the first time we’ve seen it

## Slide 21: Practices/features that have caused “unease” at GSFC
Pure Sn/insufficient Pb/prohibited materials
Board modifications (white wires, etc)
Level 3 or COTS parts
Use of bare board specs outside of our common requirements
Use of unfamiliar workmanship standards
Use of Table 2 or Table 3 materials

## Slide 22: Previous approach of handling COTS/inherited/build-to-print items
Generally bottoms up approach for each project
Standard parts control board approvals
Acceptance based on elements and processes vs component-level assessment
Emphasis on requirements, risk generally considered when push comes to shove
Rejection of modified boards based on quantity of modifications and appearance
These processes drive up cost and risk for larger spacecraft, would lead to demise of cubesat projects

## Slide 23: Transition to Risk-based approach
Early discussion about inherited items being brought to the table
Directives for proactively handling inherited items
  Based on changes from previous developments
    Design
    Environment
    Failures and anomalies
  Based on assessment of elevated risk
Component level qualification and history
Use of Commodity Risk Assessment Engineer
Focus is on “what is new” and risk areas determined from past history

## Slide 24: Standard Components CRAE
Center lead over all Standard Components responsible for
  Standard Components Commodity Usage Guidelines
  Capturing lessons learned for each project usage, from procurement, through development, to on-orbit experiences
  Interface to orgs outside of GSFC
  Determining risk for unusual usage, or for nonconforming or out-of-family standard components
  Establish testing and qualification programs as needed
Focus on applying consistent processes across all projects, emphasizing the “deltas”, and not repeating the same requests
Approval in the past may not guarantee approval on current project if the risk posture, lifetime, redundancy, or environment has changed

## Slide 25: Standard Components Commodity Usage Guidelines
GSFC-determined derating or usage limits for components
History of workmanship standards applied, expectations, and ground experiences
Known EEE parts outside of GSFC’s experience base
Known materials outside of GSFC’s experience base
Ground and on-orbit nonconformance, anomaly, and failure history
Prior risk assessments

## Slide 26: Acceptance of Inherited Items
Information provided upfront
Review and analysis
Risk Assessment performed
Risk LxC and statement provided to the CSO
CSO and Project make the call on acceptance based on risk-level
Results are documented at the Center level

## Slide 27: Inheritance Process Overview
Initiate Inheritance Plans
Perform and Document Inheritance Data and Assessments
Conduct or Support TIMS/WGs and Reviews
Refine and Finalize Inheritance Assessments
Obtain Final Inheritance SMA Endorsement and Risk Assessment
1.1 Develop Inheritance Plan:
Identify potential components (spares, COTS, Std components, Build-to-Print) that are suitable for the mission**
Determine data available from SC CRAE/ vendor/previous project.
1.2 Conduct mission suitability Analysis
Note 1: An initial SC CRAE contact meeting may be held to establish project intentions and risk posture as well as inheritance options
** Heritage type reviews may be a source for items
3.1A Conduct Inheritance Review Panel Data Evaluations and/or Risk TIMs/WGs to formulate Risk Assessments including workmanship assessment.
3.1B Conduct formal inheritance review to acquire acceptance of project risk assessments in lieu of component level PDR/CDRs.
3.2 Identify/resolve
open inheritance concerns,
action items, and
Discrepancies;
2.1 Gather and Prepare Inheritance Data Package (See Note 2) for each item or group of items
2.2 Distribute an Inheritance Data Package within 30 days of MCR/ATP
2.3 Convene Inheritance Review Panel (SC CRAE) even if no data supplied
Note 2: Include all data specified in GPR 8730.5 but at a minimum:
List of inherited items and statement of approach;
Summary results of qualification, acceptance, and/or testing completed, and comparison of current requirements;
Storage and/or Flight history of the items and specific attributes for each flight, including environments;
Ground and on-orbit performance violations anomaly and failure history including the determination of root causes;
The reliability analyses performed for the most recent version of the product.
Identification of significant changes in design, facility, process, subtier supplier, testing changes, company change of ownership, or any change from qualified unit to current unit
See GPR 8730.5 Section 4.7 for Software.
4.1 Prepare and Distribute Final Inheritance Data Package
4.2 Obtain Final Risk Assessments from SC CRAE and Inheritance Review Panel/SMEs. (See Note 3)
4.3 Update CUG with Inherited Item data gathered. (SC CRAE)
Note 3: The SC CRAE risk assessment will include resulting risk statement(s) with a likelihood and consequence in the standard GSFC 5x5 format with mitigation options or a statement that there is no elevated risk associated with use of the item I and in either cases a requirement tailoring recommendation. This will be in the form of a cover letter /memo for the final Inheritance Data Package.
5.1 Accept final SMA endorsement and Risk Assessment from SC CRAE/SMA
5.2 Include Inherited Item Risk Assessment results in upper-level milestone reviews.
5.2 Manage Risks Identified
Notes: Model after MSPSP process.
And is per GPR 8730.5

## Slide 28: Inherited items for cubesats
Many standard CubeSat components now exist
Substantial reliability benefits for using previously qualified items
However, these give rise to constraints that may increase the system design challenge
In general, it may be desirable to treat the cubesat itself as an “inherited” or COTS item
  Ensure mission success and reliability through holistic assessment, rather than piece parts approvals (alternate approach)

## Slide 29: Summary
Cubesats demand a unique approach due to a unique set of constraints
Two approaches are suggested here
  Prioritizing mission success activities by ratios of programmatic risk to technical risk and programmatic resources to technical risk
  Holistic assessment of the cubesats, where piece parts are secondary contributing elements