## Slide 1
Integrated System for Autonomous and Adaptive Caretaking (ISAAC)
Astrobee Working Group Update
Trey Smith, Maria Bualat, and the ISAAC Team
06.01.2023

## Slide 2
ISAAC update
Florida Atlantic University senior design projects
Agenda
Notes: Now switching gears to our ISAAC Phase 1X work on multi-sensor 3D mapping.
An important change here is that, in addition to targeting eventual tech transition to Gateway, we’re now targeting near-term operational use on ISS.
I’ll skip a lot of the other words here about our initial motivation for Phase 1X, except to say that it’s coming together surprisingly well… the ISS program customer interest is there, and some of these ideas are pretty far along now, as I’ll explain later.

## Slide 3
ISAAC update
Florida Atlantic University senior design projects
Agenda
Notes: Now switching gears to our ISAAC Phase 1X work on multi-sensor 3D mapping.
An important change here is that, in addition to targeting eventual tech transition to Gateway, we’re now targeting near-term operational use on ISS.
I’ll skip a lot of the other words here about our initial motivation for Phase 1X, except to say that it’s coming together surprisingly well… the ISS program customer interest is there, and some of these ideas are pretty far along now, as I’ll explain later.

## Slide 4: ISAAC Overview
Research project to develop technology for autonomous caretaking of spacecraft primarily during uncrewed mission phases
Led by NASA Ames Research Center with collaboration from Johnson Space Center
Integrate autonomous intra-vehicular robots (IVR) with spacecraft infrastructure (power, life support, etc.) and ground control
Focus on capabilities required for the Gateway that also apply to human missions to Mars and beyond
Test with existing IVR on the ISS (Astrobee, Robonaut) as an analog for future IVR on Gateway
Do not:
  Develop the IVR needed for Gateway
  Develop Gateway flight software
  (These tasks are vital but not part of ISAAC.)

## Slide 5: ISAAC FY23 Focus Areas
Phase 1XX
Technical thrust: Integrated Data
Capability area: Autonomous State Assessment
Hifi demo scenarios:
ARC: ISS demo: Astrobee close-up targeted inspection of hatch seals
JSC: Ground lab demo: Mobile manipulator inspection of freezer seals
Phase 3
Technical thrust: Coordinated Execution
Capability area: Integrated Fault Management
Hifi demo scenarios:
ARC: ISS demo: Coordinated ISS interior survey with multiple Astrobees

## Slide 6
Phase 1XX ARC: Close-Up Targeted Inspection Scenario
Close-up targeted inspection capability
  Designate a specific target site (e.g., in imagery from a previous survey)
  Astrobee autonomously maneuvers its SciCam as close as possible with the target centered
  Astrobee fine-tunes the standoff distance (~20-25 cm) to properly focus and maximize effective image resolution on the target
Broad applicability
  This capability is relevant for any task where maximum image resolution is important
  An obvious example would be inspection related to ISAAC’s original motivating scenario of a micrometeoroid-induced cabin air leak. (The leak site would likely be quite small.)
Specific application for production ISS operations:
  The ISS OSO console team reached out to the Astrobee Facility to ask whether Astrobee could perform hatch seal inspections to save crew time.
  The hatch seals are exposed to the crew cabin and could be damaged whenever the hatches are open (as they usually are)
  Since hatch closure would be used as an emergency hazard mitigation for some catastrophic hazards, hatch seal damage significant enough to cause a leak would be taken very seriously
  Hatch seals are presently inspected by crew about twice a year
Activity to date
  As a late-breaking change to ISAAC Phase 1X, secondary hatch seal inspection tasks were added to mapping activities ISAAC9, 10, and 11. ISAAC/Astrobee worked with OSO to iterate, improving targeting and image quality.
  OSO’s most recent evaluation is that the Astrobee hatch seal inspection demonstrated to date is not yet ready to be deployed for production use, but they are interested in further evaluation if the inspection process can be improved (potential improvements to image quality and analyst user interface for image review)
F
F: Divot and cut
~1.8 x 1.5 mm
G
G: Divot
~0.7 x 0.3 mm
These Astrobee photos confirmed previously known hatch seal damage sites (ISAAC11, 2022/06/16). A new “focus stack” ops approach was used to get improved focus on the targets, yielding Astrobee’s highest-resolution ISS images to date (~0.1-0.2 mm).

## Slide 7
Phase 1XX ARC: Technical Development
Bumble performing a close-up inspection of a hatch seal in USL during ISAAC-11 (2022/07/11)
Task | Status
Close-up targeted inspection | 
Target selection: Develop an interface for ISS ops staff to select targets for close-up inspection using panoramic imagery from a previous ISAAC-style Astrobee survey | In work, see next slide
Precision targeting: Improve Astrobee’s capability to image a precise target location, potentially making use of prior imagery of the target to center it in the camera field of view. | Initial software version developed. Currently planning to rely on Astrobee general-purpose localization. Inspection algorithm optimizes viewing direction considering obstacle constraints.
Precision focus: Improve Astrobee’s capability to precisely focus on a specific target, potentially adjusting standoff distance using its HazCam depth sensor. | Initial software version developed. Refining conops for focus in high-relief situations. Needs further testing in Astrobee Granite Lab prior to ISS.
Context imagery: Develop an interface for ISS ops staff to view the resulting high-resolution image “postage stamps” located in context relative to prior survey imagery to aid interpretation. | Not started yet. Interface will likely derive from target selection interface.
Change & anomaly detection | 
Develop a flexible framework that enables an analyst to define and detect events of interest in Astrobee survey data | Framework core interface set up. Work on Phase 1XX ISS demo scenarios not started yet.

## Slide 8: Phase 1XX ARC: Target Selection Interface Prototype
1
2
3
4
5
Select a panorama near the target of interest using the ISS overview map.
Use intuitive mouse/touch controls to pan and zoom within the selected panorama.
Camera icons indicate the centers of the individual Astrobee SciCam image frames that were stitched to form the panorama. Select the image closest to your target.
Use one of the provided drawing tools (point, rectangle, polygon) to annotate a region of the image to target for inspection. The pixel coordinates will be converted to 3D positions for Astrobee to target.
Add details about the target (e.g., motivation, priority, what you want the analyst to look for in the resulting imagery).
Save your annotations and submit to the Astrobee Facility to convert to an Astrobee ISS targeted inspection plan.
6
These images are screen shots from a functional prototype web interface. More maturation is needed before release. Steps 3-6 are new.
Notes: Title - Provide a title for any noteworthy highlight/accomplishment
Type – Milestone, EPO, Test, etc..
Element – Portfolio Project: Specific Facet. Other: Map to Tech Assessment / Tech Element / Tasks
Provide your description.
New Image for EPO – Yes – Project Overview Slide or No.
Highlight Submitted – No, Yes, Will submit on XX/XX/XXXX.

## Slide 9
Phase 1XX ARC: Astrobee ISS Campaign
JEM
NOD2
COL
USL
NOD1
NOD3
PMM
Act # | Ph. | Objective | Module | Date *
12 | 3 | Multi-sensor mapping coordinated execution | JEM | 2023/12/06
13 | 1XX | Targeted inspection | USL | 2024/01/03
14 | 3 | Multi-sensor mapping coordinated execution | USL | 2024/01/31
15 | 1XX | Targeted inspection | USL | 2024/02/21
16 | 1XX | Targeted inspection | USL | 2024/03/13
13
14
15
16
12
* Dates approximate, requested in Inc70 1-pager
3 of 5 requested activities allocated to Phase 1XX

## Slide 10
Aim for near-term infusion of ISAAC multi-sensor mapping to operational use with Astrobee on ISS in addition to medium-term use on a future Gateway IVR platform
Autonomous robotic multi-sensor mapping can provide several operational benefits to ISS:
  Save crew time. Autonomous robotic data collection could partially replace the need for crew safety videos (although Astrobee can’t cover all parts of the ISS)
  Provide more accurate and timely information. The ISS interior is a very dynamic environment, and the robot could collect map updates more frequently than the current tempo of crew safety videos (once every few months).
  Enhance usability. Enable users to navigate directly to the area of interest in a 3D model of the ISS, rather than downloading a massive video file and scrubbing through it to find the area of interest
  Provide new “superpower” senses. In the near term, we propose to enhance ISAAC maps with sound source information from the SoundSee microphone array payload for Astrobee. Going forward, the ISAAC mapping framework can easily accommodate new sensor payloads added to Astrobee.
  Enable automated change and anomaly detection. Automated detection of many types of anomaly (e.g., hardware intruding into a keepout zone) requires understanding the scene geometry and naturally builds on ISAAC’s 3D map building. Without automation, labor-intensive manual review of safety videos is presently slow enough that by the time the review is done, its recommendations are often obsolete.
Initial candidate ISS use cases for map data:
  Safety: Check keepout zone violations, hatch seals, Emergency Egress Guidance System visibility, translation paths, and other items.
  Logistics: Spot check the locations of cargo. Review available capacity of stowage locations. Correlate data from RFID Recon payload and update Inventory Management System database.
The ISS program is currently considering a proposal from the Astrobee Facility team to perform Astrobee surveys of the USOS every six months, starting in January 2023
  Further ISAAC development is needed to streamline operations and post-processing so the Astrobee Facility can support this service going forward
Phase 3 ARC: Coordinated Multi-Robot Mapping Scenario
Bumble and Queen operate side-by-side to map USL during ISAAC-11 (2022/07/11)

## Slide 11
Phase 3 ARC: Technical Development
Astronaut Chris Cassidy poses with Bumble and Honey Astrobees on ISS
Astrobee localization is complicated by areas of the prior map that have fewer features (red)
Task | Status
Multi-robot coordination | 
Demonstrate coordinated multi-robot automated task planning and execution with two Astrobees on ISS | Software development in work.
Automated multi-robot planning will be available for future Astrobee platform users as part of ISAAC open-source release | Happens automatically with ISAAC rolling open-source release
Astrobee Robot Software improvements | 
Begin migration to ROS 2 framework with better quality assurance, potentially enabling future software infusion into robot platforms with more mission-critical capabilities | Well under way. Core modules and software sim migrated.
Robust map-building: For post-activity automated map registration, improve reliability and require less manual oversight, requiring less processing time between survey activities | Some automation improvements already available for Astrobee Facility’s standard navigation map updates. Others in work.
Robust navigation: Improve overall Astrobee navigation, especially including sparse map localization reliability | Software development in work.
Gather recommendations for future IVR software architecture based on ISAAC experience | Not started yet.

## Slide 12: Why Move to ROS2?
ROS = Robot Operating System
ROS1 will be deprecated in 2025
New tech developments from industry players moving to ROS2
Space ROS (kicked off via Blue Origin ACO) is an open-source extension of ROS2 designed to support robot flight software
S. Macenski, T. Foote, B. Gerkey, C. Lalancette, W. Woodall, “Robot Operating System 2: Design, architecture, and uses in the wild,” Science Robotics vol. 7, May 2022.
ROS1
Widely Used for Research
EOL in 2025
ROS2
Terrestrial Industry Standard
Space ROS
Space Cert. S/W
Features | ROS1 | ROS2 | Space ROS
Swappable middleware |  | ✓ | ✓
Multi-platform |  | ✓ | ✓
Built-in network security, authentication, quality of service |  | ✓ | ✓
Additional aerospace-focused V&V |  |  | ✓
Artifacts for NPR 7150.2 certification / analysis |  |  | ✓

## Slide 13
Phase 3 ARC: Astrobee ISS Campaign
JEM
NOD2
COL
USL
NOD1
NOD3
PMM
13
14
15
16
12
2 of 5 requested activities allocated to Phase 3
Act # | Ph. | Objective | Module | Date *
12 | 3 | Multi-sensor mapping coordinated execution | JEM | 2023/12/06
13 | 1XX | Targeted inspection | USL | 2024/01/03
14 | 3 | Multi-sensor mapping coordinated execution | USL | 2024/01/31
15 | 1XX | Targeted inspection | USL | 2024/02/21
16 | 1XX | Targeted inspection | USL | 2024/03/13
* Dates approximate, requested in Inc70 1-pager

## Slide 14: Project Schedule
We are here
FY24
* Timeline edits rough, don’t try to read exact dates
VIPER
Almost the entire ISAAC team is currently on a 6-month hiatus, working to help the VIPER mission software development get back on schedule

## Slide 15: Project Summary
Phase 1XX
ARC: ISS demo: Astrobee close-up targeted inspection of hatch seals
JSC: Ground lab demo: Mobile manipulator inspection of freezer seals
Technology
Close-up targeted inspection
Change & anomaly detection
Mobile manipulator
Compliance/admittance control
Phase 3
ARC: ISS demo: Coordinated ISS interior survey with multiple Astrobees
Technology
Multi-robot coordination
Begin migrating to ROS 2
Map-building and navigation

## Slide 16
ISAAC update
Florida Atlantic University senior design projects
Agenda
Notes: Now switching gears to our ISAAC Phase 1X work on multi-sensor 3D mapping.
An important change here is that, in addition to targeting eventual tech transition to Gateway, we’re now targeting near-term operational use on ISS.
I’ll skip a lot of the other words here about our initial motivation for Phase 1X, except to say that it’s coming together surprisingly well… the ISS program customer interest is there, and some of these ideas are pretty far along now, as I’ll explain later.

## Slide 17: FAU Design Course
NASA’s Astrobee/ISAAC projects are acting as a “client” for a year-long senior design course at Florida Atlantic University
  Brian Coltin is the lead POC from the NASA side, with support from Marina Moreira and Trey Smith
  Prof. Zhen Ni at FAU is the course instructor
The course covers two academic terms (Fall 2022 + Spring 2023)
  The baseline expectation is that each multi-disciplinary student design team of 4-5 undergrad seniors will produce a design during the first semester and some prototype hardware during the second semester
As the NASA/Astrobee topic was popular with the students, two student teams were assigned to work with us. The selected project objectives are:
  Team 1: Design a thermal infrared camera payload for Astrobee.
    Because the Astrobee robots can autonomously survey the ISS interior without requiring significant astronaut time, deploying an Astrobee thermal camera could potentially enable regular thermal mapping of much of the ISS, as well as targeted thermal inspection on demand.
  Team 2: Design a cargo berth fixture for temporarily parking cargo bags during transfer ops
    Astrobee can transfer cargo bags, but doesn’t have the dexterity to manage typical restraint harnesses, bungees, etc. The cargo berth fixture would mount to a wall and provide a place for Astrobee to temp stow and retrieve bags using visual guidance for mating and a bag retention system that Astrobee can release remotely.
Future:
  At present, this is an exploratory side-project
  There is no funded effort to mature and launch these payloads
  If the prototyping effort goes well, it might be worth performing integrated payload testing with an Astrobee ground unit and seeking funding for further work.

## Slide 18: Thermal Infrared Camera Project - Ocelli
Context: ISAAC/Astrobee tech already enables ISS interior survey.
Vision: Capture additional thermal imagery during the survey and register the data with other map layers.
Potential applications: Find hot spots (component overcurrent, ventilation underperforming) and cold spots (cabin air leak, freezer not sealed properly)
Prototype risk reduction: Figured out geometric and thermal calibration of the thermal camera, demonstrated registration with a depth sensor analogous to the Astrobee HazCam.
Ocelli​
FLIR Lepton 3.5 Thermal Camera
Raspberry Pi 3B+ mprocessor inside 3D printed housing
KinectV2 RGB-D sensor (analog to Astrobee HazCam)
+
=
Thermal Image
Point Cloud
3D Thermal Overlay
Alex Zambony-Mehta​
Roger Reyes​
Matheus R. Melo​
Gianni Difede​
Jordan Diaz

## Slide 19: Cargo Berth Fixture Project – Astro-Berth
Context: Astrobee can move cargo bags but can’t temp stow and retrieve them.
Vision: Low-profile berth fixture for cargo bag provides passive magnetic retention with remotely controllable release, and optional visual guidance to assist bag mating.
Potential applications: Enables free-flyer to assist with cargo transfer between Gateway and visiting cargo vehicles during uncrewed phases (manipulator robot still needed to unbuckle bags, but free-flyer can fly the bags across the vehicle)
Prototype risk reduction: Got through many integration challenges to yield a working demo of guided blind mate operation with releasable magnetic retention
Febert Pierre Louis
Tyler Davis
Kory Parris
Levi Throop
Ryan Font
Astro-Berth
Magnetic retention with remotely controllable release
Camera for visual guidance
Wake-from-hibernate on modulated light signal
Prototype hardware

## Slide 20
QUESTIONS?