## Slide 1
6/1/23
REALM-2 Project
Radio Frequency Identification (RFID) Reconnaissance (Recon) Payload
Andrew Chu
NASA/JSC
Andrew.chu-1@nasa.gov
281-483-1445
This publication does not contain information which falls under the purview of the U.S. Munitions List (USML), as defined in the International Traffic in Arms Regulations (ITAR), 22 CFR 120-130, and is not export controlled. This publication does not contain information within the purview of the Export Administration Regulation (EAR), 15 CFR 730-774, and is not export controlled. This publication is not intended for distribution outside of the NASA and International Partner communities. Release to the public requires approval through the appropriate NASA Release Process (e.g., FOIA, NASA STI, etc.).
Notes: <number>

## Slide 2: Experiment Overview
RFID Recon is an RFID reader that is installed in the bottom forward payload bay of Astrobee. It is the second phase of the REALM (RFID Enabled Autonomous Logistics Management) project.
  Phase one of REALM (REALM-1) is RFID Logistics - a fixed RFID system on ISS located in Node 1, USL, and Node 2 that has been operational since Feb 2017.
  Phase three of REALM (REALM-3) is RFID Smart Sensing – an RFID outfitting of a Zero-Gravity Stowage Rack (ZSR) already in use in the USL. Installed Sept 2022.
Primary objectives of RFID Recon:
  – Expand RFID coverage to RFID Logistics non-instrumented modules, as well as nulls in instrumented modules
  – Refine localization estimates
    Additional Complex Event Processing (CEP) context for RFID Logistics localization engines on ground (i.e., additional fixed reader)
    Search for a specific tag
Onboard ISS in Nov 2019 (NG-12)
June 1, 2023
Export Control: See first page.
<number>

## Slide 3: RFID Recon Installed on Astrobee
Propulsion Module Antenna embedded in left and right skins
RFID reader with 2 antennas
June 1, 2023
Export Control: See first page.
<number>

## Slide 4: Accomplishments
June 1, 2023
Export Control: See first page.
<number>
Commissioned with Astrobee in JPM on 1/29/21
  Tested basic functionalities:
    Able to read RFID tags
    Can move Astrobee along waypoints
    Verify that we will not transmit in implemented Quiet Zone
    Home in on a Cargo Transfer Bag (CTB) placed in front of Astrobee
ISAAC – participated on 3 mapping missions of JPM on 2/23/21, 3/26/21, 4/19/21

## Slide 5: Accomplishments - continued
REALM-1 instrumented modules
(2 readers + 8 antennas in each module)
RFID Recon Science-1 mission on 8/6/21
  Crew installed our hardware and translated Astrobee to PMM and perch Astrobee at PMM hatch on handrail. Astrobee was perched for 3.5 hours and then crew moved Astrobee back to JPM.
June 1, 2023
Export Control: See first page.
<number>
Notes: December 2008
<number>

## Slide 6: Accomplishments - continued
RFID Recon Science-2 mission 9/7/21
  Perform homing missions in JPM to expand on basic homing mission during commissioning
    Homing routine should determine direction of targeted RFID tagged item to rotate Astrobee and drive Astrobee toward item
    The homing plug-in rotated Astrobee away from expected direction
  Post-mission, recreated inverted pitch and yaw rotations on the ground and corrected the homing plug-in
  Testing at Astrobee granite lab confirmed original plug-in error and verified plug-in fix
RFID Recon Science-3 mission 12/6/21
  Re-run Science-2 mission with corrected homing plug-in.
  Homed into CTB with target tag 3 times from 2 different Astrobee starting location.
June 1, 2023
Export Control: See first page.
<number>
Notes: December 2008
<number>

## Slide 7: Accomplishments - continued
RFID Recon Science-4 mission 4/6/21
  Performed inventory while perched at 4 locations in JPM. Locations were selected to inventory areas with stowed items: at NOD2 hatchway, in bays 2 and 5, and in bay 6 looking into the JLP.
  Performed inventory down centerline of JPM. Error prevented us from flying Astrobee through the waypoints, but crew moved us from location to location.
June 1, 2023
Export Control: See first page.
<number>

## Slide 8: Accomplishments - continued
RFID Recon Science-5 mission 10/25/22
  Astrobee docked with crew transferring cargo between JPM and COL through NOD2
    Emulate tracking of cargo transfers between the Gateway Logistics Module and Human Landing System through the Habitation and Logistics Outpost (HALO).
    Allows us to determine best configuration of the Gateway readers without doing a lot of testing after we are on Gateway.
  Plan was to test 3 configurations of RFID readers in NOD2 (reader in Gateway mode, various power levels, number of antennas used).
    Plan failed because changing to the Gateway mode caused the NOD2 readers to go to STBY.
      Post mission, failure traced to Virtual Machine for NOD2 readers upgraded a few hours before mission with one that did not include default command file update.
      Able to test 2 scenarios with reader in ISS mode: 1) both NOD2 readers ON and 2) one NOD2 reader OFF
June 1, 2023
Export Control: See first page.
<number>

## Slide 9: Future Plan
June 1, 2023
Export Control: See first page.
<number>
  Re-run Science-5 mission with readers in Gateway mode

## Slide 10
Backup
June 1, 2023
Export Control: See first page.
<number>

## Slide 11: RFID Recon Reader Module
Antennas (2)
Fans (2)
Connections to Propulsion Module antennas (2)
Magnets (4)
SD card slot
Reader mounted antennas (2)
Fans (2)
Connections to Propulsion Module antennas (2)
SD card slot
June 1, 2023
Export Control: See first page.
<number>

## Slide 12: Propulsion Module Antenna Bumble Skins
June 1, 2023
Export Control: See first page.
<number>

## Slide 13: REALM-1: RFID Logistics Awareness Overview
1st Goal: localize tagged cargo with ½-module resolution or better using fixed RFID coverage zones
6 fixed RFID readers and 24 antennas in 3 modules
3 instrumented modules for experimental phase: N1, USL, N2
  Primary pathway for cargo translation following offload of visiting vehicle
Data is downlinked to the ground for archival, mining, and Complex Event Processing (CEP)
downlink
PMA-3
N2
COL
JPM
JLP
LAB
N3
N1
A/L
ФГБ
PMA-1
Z1
FGB
PMA-2
PMM
June 1, 2023
Export Control: See first page.
<number>
Notes: <number>

## Slide 14: RFID Recon Con-Ops: Missions
Astrobee Docking Station
JSL
HOSC
RFID Recon
Control Station
CEP System
Mission
Package
RFID Recon Mission Types
A - Teleoperation
B – Perched Astrobee
C – Inventory
D – Tag Search
E – CEP Context
F – Map RFID Logistics fields
G – RFID Sensing*
H – 6-DoF WHISPER System*
*Hooks only - not currently in scope
IMS Clone
Autonomous
June 1, 2023
Export Control: See first page.
<number>