## Slide 1: Environmental Monitoring Microsensor Array (EMMA) for Free Flying Robots
Phase II SBIR
Contract: 80NSSC21C0621
Astrobee Working Group June 1, 2023
Makel Engineering, Inc.
James Makel PhD
Darby Makel PhD, PI
Frank Wangberg - Embedded Systems
Richard Kokoletsos - Mechanical Design
Elaine Kuang – Research Chemist
Ethan Robinson – Software Engineer
NASA COR: Jose V. Benavides, NASA Ames
Contact:
Dr. James Makel
jmakel@makelengineering.com
530-801-2232

## Slide 2: EMMA Payload Motivation and Objectives
Objective: Provide mobile smart sensing capability to support autonomous habitat monitoring
Sensors:
  Chemical: O2, CO2 ,CO, H2, NH3, VOCs
  Environmental: Pressure, Humidity, Temperature
  IR and Visual Cameras and Sound
Data Analysis:
  Integrated machine learning capability interprets sensor data and sends alerts autonomously
Development Work:
  Targeting development work toward important use cases on Gateway and ISS
  Developing and delivering prototypes to NASA for testing
  Transitioning to an ISS Flight Demonstration as EMMA matures

## Slide 3: Key EMMA Use Cases
Air Quality and Revitalization Monitoring
  CO2 and O2 monitoring
Chemical Leak Detection
  Thermal management/cooling systems using working fluids such as ammonia
  Hydrogen release from batteries, fuel cells, water processing systems such as electrolysis
  CO, H2, or CO2 from water recovery Sabatier reactors
Precombustion/Early Fire Detection
  Overheating of electronics
  Outgassing
  Potential classification of materials
Flexible Platform for Sensor Integration

## Slide 4: EMMA Prototype Specifications
Feature | GEN-1 EMMA | GEN-2 EMMA
Measurements and Ranges |  | 
Solid State Chemical Sensors | O2 0-96% CO 0-10 ppm H2 0-5% NO2 0-5 ppm | O2 0-96% CO 0-10 ppm H2 0-5% NO2 0-5 ppm
NDIR Chemical Sensors | CO2 0-3000 ppm | CO2 0-3000 ppm NH3 0-200 ppm CO 0-2000 ppm
VOC Sensors | VOC 0 - 10 ppm | VOC 0 - 10 ppm
Environmental Sensors | Pressure 0.5 to 16 psia Humidity 0-95 RH (-40 to 30 °C DP) Temperature -20 to 50 °C | Pressure 0.5 to 16 psia Humidity 0-95 RH (-40 to 50 °C DP) Temperature -20 to 50 °C
IR Camera | FLIR Lepton | FLIR Lepton
Imaging Sensor | 720p Visible Camera | 1080p or higher res Camera
Audio | Microphone (60 to 15 kHz) | Microphone (60 to 15 kHz)
External Connectivity | Communications to Astrobee HLP | Communications to Astrobee HLP Bluetooth hub for 3rd party device connection to Astrobee
Other Specifications |  | 
Power | 14.4VDC, 0.90 A | 14.4 VDC, 0.40 A
Envelope | 5.9 in x 4 in x 1.8 in | 5.9 in x 4 in x 1.8 in
Mass | 520 grams | Under 400 grams

## Slide 5: Sensing Technology: Electrochemical and Optical
O2 Sensor
H2 Sensor
CO Sensor
Miniaturized Solid-State Chemical Sensors
Multi-Species NDIR
2.7”
1.9”

## Slide 6: Sensing Technology: Photoionization and Camera
FLIR Camera
Visual Camera
Image Overlay
Photoionization
Detector
Visible Light Image
Thermal Image
Photoionization Detector for Volatile Organic Carbon (VOC) Detection
+
=
Thermal and Visible Imaging

## Slide 7: EMMA GEN-1 to GEN-2 Evolution
Pumps
Analog Single Species NDIR
Micro-GC
Electrochemical Sensors
IR Camera
Visible Camera & Microphone
VOC PID Sensor
Valve
Electronics
Pressure & Humidity
Sensors
Gas Inlet
Pressure & Humidity
Sensors & Microphone
Visible Camera
IR Camera
Electrochemical Sensors
VOC PID Sensor
Valve
Micro-GC
Pump
Digital Multiple Species NDIR
GEN-1 Prototype
GEN-2 Prototype

## Slide 8: Integration with Astrobee
EMMA Payload Analyzes Data
Threshold and Anomaly Alert Messages Sent
EMMA Android Application Manages Payload
Astrobee Coordinates and Payload Configuration Sent
Autonomous Habitat Monitoring Systems/Ground Control
Manual Control
Habitat State Reported

## Slide 9: Flight Mission Types
Ride-along Mission
  Collect useful data while Astrobee performs other tasks
Patrol Mission
  Patrol entire habitat to learn normal conditions and locate anomalies
Loiter Mission
  Monitor fixed location or small area of interest over time
Response Mission
  Investigate area in response to detection and commands from other autonomous systems

## Slide 10: Sample Concept of Operations Leveraging Machine Learning
Normal Habitat Conditions
Local Anomaly
Recognized
Algorithm accurately reconstructs measured chemical signatures
Algorithm cannot accurately reconstruct unfamiliar chemical signatures
Not Recognized
Analyze chemical measurements on patrol
Learn to recognize typical normal chemical signatures
Unrecognized chemical signatures are flagged as anomalous

## Slide 11: EMMA Development Progress and Plans
GEN-1 EMMA Delivered November 2022
    Expanded sensing capability for GEN-1 versus Phase I prototype
    GEN-1 includes hardware suitable for running machine learning algorithms for autonomous anomaly detection
GEN 2 Prototype Development Is Underway
    Reducing power consumption by adding capability to switch off peripherals and optimizing solid-state sensor packaging
    Continuing to evaluate additional sensing capability (acid gases, particulate)
    Developing EMMA Android app to run on Astrobee High Level Processor (HLP)
    Maturing data storage and processing procedures for machine learning algorithm training
    SSP 57000 Pressurized Payloads Interface Design Requirements
    EMI per DSG-RQMT-007