## Slide 1: Astrobee System Overview
SPHERES/Astrobee Working Group
August 23, 2017

## Slide 2: Astrobee Elements
Astrobee
Free Flyer
Dock
Ground Data System

## Slide 3: System Data Flow Diagram
Queen
Honey
Bumble
JSC MCC
Ethernet/LAN
WiFi:
Payload LAN
Ethernet: Internal IP
Ethernet: Internal and Payload LAN
ISS
LLP
MLP
NAS
Ku-Band
MSFC
ARC MMOC
White Sands
Operator Control
Operator Control
(POIC)
Operator/Engineer Control
Crew Control Station
Storage
HLP
Payload
Dock
JSL
Payload LAN
Payload LAN Switch
5GHzWAP
Other/LAN
Link Legend
USB
Internal
Switch
Internal
Switch
Dock CPU
Ground Relay
(HOSC)
GS Inst
Operator Control
Notes: All processors inside Astrobee are on a private network, connected via an internal 100Mbit switch.
  All internal processors have an internal IP address that is not routed outside of Astrobee & Dock when docked.
  Internal IP addresses are used for internal FSW communications.
Both the MLP and HLP have JSL-assigned IP addresses for both their wired and wireless interfaces.
  The wired addresses are only accessible when docked.
  The wireless addresses are generally always accessible.
MLP WiFi is used for telemetry and commanding to GDS.
When docked, the wired IPs are used for large file transfers, software upgrades, and anything that requires high reliability.
  Wired and wireless IPs are both active when docked.
HLP WiFi is enabled and used for .
  Redundant interface to access the freeflyer if the MLP interface dies.
  Streaming HD video to the ground.
  Possible use is for Guest Science. (See FSW)
Payloads interface via USB to the HLP
  Should they use a USB-to-Ethernet solution, they are isolated from the rest of the network.
The dock will be attached to an ISS Router, which can flow down to the ground via KU-band over JSL-2 to MSFC.
The dock also has an internal computer that is attached to the Payload LAN and Astrobee. It has both an internal Astrobee IP and a Payload LAN IP.
The WiFi modules associate with the JSL PayloadLAN WAPs, which also route to the ground via KU-band over JSL-2 to MSFC.
We are relying on KU-IP-Services to route data to the ground over an IP-network built on the CCSDS foundation of KU-band.
A ground relay is located in MSFC HOSC to help with data relay to multiple control stations.

## Slide 4: Astrobee
Corner Bumpers
Impeller
Nozzle
Laser Pointer
Speaker/Microphone
Battery
Terminate Button
Power Switch
Wake Button
Forward Flashlight
Status LEDs
SciCam
NavCam
HazCam
Touch Screen
Signal Lights
SpeedCam
Arm
DockCam
PerchCam
Aft Flashlight
Notes: SPHERES is very popular, but also due for an upgrade. IRG is leading the design of Astrobee to replace SPHERES.

## Slide 5: Payload Attachment Options
“Lock” Position
“Un-Lock”
Position

## Slide 6: Dock
AR Target
Air Vent Deflector
Main Power Breaker
Cooling Fan
Cooling Fan Screen
RJ-45 Connector
Power Connector
Free Flyer Berth
Subsystem Breakers

## Slide 7: Plan Editor Tab (Operator/Engineering)
Plan info
Element editor
List view of Plan
Notes: Added floating camera controls. Added Docking Station connection light. Added Plan Description. Rearranged buttons in top right panel.

## Slide 8: Run Plan Tab (All)
Model of loaded plan
List view of loaded plan
Select valid plan and upload to Astrobee

## Slide 9: Teleoperation Tab (All)
Drag preview to adjust movement command
Buttons here can be changed via config file
Send movement command
Construct movement command
Adjust settings

## Slide 10: Guest Science Tab (Crew)
Monitor Astrobee positions in 3D window
Command Astrobees
Status summaries
Names of loaded Plans
Checkboxes select Astrobees to command

## Slide 11: Advanced Guest Science Tab (Operator/Engineering)
Select APK to see Status
Start and Stop APKs directly
Preview and change APK command before sending
View detailed telemetry from APKs

## Slide 12: Advanced Tab (Engineering)
Detailed Health and Status
Triggered and Not Triggered Faults
View and change Operating Limits
Detailed battery status
Detailed component status
Configure telemetry sent to Control Station
Disk usage
View and configure data saved to disk

## Slide 13: Astrobee Status
Finalizing drawings
Procurement has begun
On track for August 31st delivery:
  Beta release of Flight Software/Simulator
  Mechanical Payload ICD drawings
  Initial draft of the Guest Science Guide