## Slide 1
Lorenzo Flückiger
Maria Bualat
Intelligent Robotics Group
NASA Ames Research Center
Lorenzo.Fluckiger@nasa.gov
Astrobee Robot Software (ARS) SPHERES/Astrobee Working Group, 08/23/2017

## Slide 2: Astrobee Elements / ARS
Astrobee
Free Flyer
Dock
Ground Data System
Users Development Testbed
Astrobee Robot Software Scope

## Slide 3: ARS (Astrobee Robot Software) Overview
ARS is deployed on 4 cell phone type processors (Astrobee + Dock) running Linux and Android
Astrobee contains 7 distinct microprocessors with custom firmware + several microprocessors with COTS firmware
Software deliverables includes:
  Custom firmware(s)
  Custom tailored Linux kernels
  Linux and Android Operating Systems
  ARS dependencies (third-party libraries)
  ARS Source Code  Open Source

## Slide 4: ARS Features
Manage Astrobee sensing and actuation
Localize and Navigate within the ISS
Perform autonomous docking (+ return to dock)
Perform autonomous perching
Support teleoperation from ground
Support plan based automated tasks
Support “Guest Science” operations
Support multi Astrobees communication
Support hardware for multisensory human interaction
less mature

## Slide 5: ARS Components
OS (Communication Framework)
Localization
  Marker less Flying
  Docking
  Perching
Offline mapping for localization
Pose Estimation + Propulsion Control (GNC)
Executive
  Mode Management
  Sequencer (Plan Execution)
Mobility
  Generates and validates trajectories
  Performs collision detection
Fault Management
Guest Science
User Interfaces Support
Simulator
Platform Management and development tools
SLOC Directory SLOC-by-Language
1367376 gnc cpp=1367280
45474 submodules ansic=20471,java=7963
14262 mobility cpp=14015
12351 localization cpp=11923
9803 hardware cpp=9366
6760 scripts python=3527,sh=1844
6393 shared cpp=6344
6279 management cpp=6090
4778 tools cpp=2290,ansic=984
3600 communications cpp=3524
Totals grouped by language:
cpp: 1422365 (96.05%)
without autogen: 58305
ansic: 21455 (1.45%)
xml: 14956 (1.01%)
python: 9792 (0.66%)
java: 7963 (0.54%)
sh: 2867 (0.19%)

## Slide 6: ARS and ROS
ARS makes extensive use of the open-source Robot Operating System (ROS):
  Communication framework linking all “nodes” running on the target platform
  Try to maximize the re-use of existing ROS messages benefit from existing ROS packages
  Use ROS introspections tools to rapid debugging
  Use ROS facilities to record/replay/analyze data
  Use some ROS/Gazebo components for the simulator

## Slide 7: Simulator
Custom propulsion system and some localization sensors
Gazebo based dynamics model, imagers, arm, lights and ISS model
Can run all nodes on desktop or some nodes on target development board

## Slide 8: ARS APIs Overview
ARS uses ROS within Astrobee: Messages, Services and Actions define the internal API
Astrobee & Ground communication uses DDS and the RAPID framework for command and telemetry
Commands:
  Commands are defined using XP-JSON schema, tools auto-generates RAPID command dictionary
  ARS defined a ”ROS Command” mirroring the DDS command structure
  Onboard Astrobee Guest Science or Ground Applications share the same command dictionary (some commands unique to one client) with either DDS or ROS transport
Telemetry:
  Internal uses ROS Messages (using ROS messages when possible)
  External uses DDS Messages (subset only, re-using RAPID messages)

## Slide 9: ARS APIs Access
DDS Bridge
Operator Access Control
Executive
Subsystem
Subsystem
Subsystems
Guest Science App (HLP)
Control Station
ROS messages
ROS messages
RAPID Commands (DDS)
RAPID Msgs (DDS)
ROS “Command”
ROS “Command”
Services, Actions or Topics (all ROS)
MLP LLP

## Slide 10: First Open Source Release
First “Beta” release: 0.1.0 scheduled for 08/31/17
  Goal: provide an early preview on how to interact with the software
  Some components are very mature
    Communication framework, Mapping, Localization, Control, Mobility, Executive, Fault Management framework
  Not feature complete (low risk components)
    Prototype of Guest Science [October 2017]
    Draft Astrobee to Astrobee communication [January 2018]
    Platform management (data down/upload, etc.) [April 2018]
    User Interfaces support (Android) / signal lights [April 2018]