## Slide 1: Guest Science and Simulator Integration
Andres Mora

## Slide 2: Simulator
Simulator:
  Has the same code base as that in the robot
  Adds components to simulate the environment inside the ISS and the communication with ground control
  Allows users (Guest Scientists) to quickly test their experiments and understand how the robot would behave.
Robot:
  Hardware includes multiple cameras, processors, actuators, and mobility mechanisms.
  Software allows localization within ISS, communication, grasping, actuation, locomotion.
  Runs Guest Science payload (both hardware and software)
Robot
Environment
Comms
Simulation Concept

## Slide 3: Simulator
Developers require:
  Simulator able to run in a medium to high-end laptop (e.g. Nvidia Quadro K1100M – Dedicated Video Memory 2048MB GDDR5)
  Linux environment (Currently Ubuntu distribution, LTS 16.04)
  Integrate ROS, Android (Android Studio) operating systems
  Simulator is based on C++, Simulink deployed C blocks
  Developers in Android extensively use multiple programming languages: Java, XML
  Provides 3D representation of the robot via Rviz and/or Gazebo
  Provides dynamical, sensor models via Gazebo

## Slide 4: Software Architecture
Three ARM processors to isolate guest scientist code, vision based localization and GNC loop, connected by 100Mbps network switch
High Level Processor (HLP) – Android, Quad core
  Interface with Science Camera and Display
  Encodes video with dedicated hardware
  Runs guest science code
Mid Level Processor (MLP) – Linux, Quad core
  Runs absolute localization algorithms, obstacle detection, communications
  Heavy processing power used by vision
Low Level Processor (LLP) – Linux, Dual core
  Runs 62.5 Hz: EKF and propulsion control loop
Simulator
ROS messages:
ISS Environment
LLP
MLP
HLP
Astrobee
Sensing/Actuation:

## Slide 5: Guest Science
Guest Science interface scenarios
Basic API (Zero Robotics): handles high-level commands and uses Android environment only
Intermediate API (Zero Robotics, University researchers): high-level to mid-level commands by-passing Android-ROS bridge but still using Java-ROS framework. Telemetry is accessible.
Advanced API (University researchers): By-passes completely provided Java-ROS framework.
Notes: Basic API, Intermediate, Advance API

## Slide 6: Guest Science Implementation
Simulator or MLP
Android (Emulator or HLP)
svc
Executive
ARS Lib
ROS Java
app
ARS Java API
ARS Android LIB
Guest Science Application Code
ARS Android SVC
app
Guest Science
Manager
ARS Java API
ARS Lib .
ROS Java
GS Mgr.
Stub
process
Guest Science Application Code
Not available in first release
Pure Java
Model can be used on Android too if packaging ROS Java + ARS Lib in App
Higher fidelity simulation with the Android platform emulated

## Slide 7: Android Guest Science
Android-ROS Bridge
Service App
Android Guest Payload App
Android
HLP
Executive
ROS/Java
Communication between different processes/threads
Intercommunication Process (IPC)
Services:
  Scheduled
  Started
  Bound
Messenger class to avoid complex AIDL implementations
MLP

## Slide 8: Android-based Guest Science Demo