## Slide 1: Assistive Free-Flyers with Gecko-Inspired Grippers for Automated Logistics in Space
PI: Mark Cutkosky
Co-I: Marco Pavone
Consultant: Dr. Jeff Hoffman, MIT
February 28, 2018

## Slide 2: Motivating Goals
Assistive free-flyers on the ISS
  Perching for inspection/monitoring
  Tool retrieval, return
  Unpacking cargo
Complex in-space manipulation and proximity operations tasks
  On-orbit servicing, assembly
  Debris removal
  EVA assistance
SPHERES
Astrobee
Restore-L Servicer
AERCam Sprint
Notes: Goal: Enable complex grasping and manipulation maneuvers that can be performed autonomously in space
- This will be a step towards performing many other complex but important robotic tasks in space (these are examples)

## Slide 3: Adhesive Grippers
Key idea:
Directionally-aligned microfeatures create van der Waals adhesion under shear stress
Two opposing pads form a surface gripper
Advantages:
Versatile: Able to grasp without enclosing
Gentle: Very low attach/detach forces
Dynamic: Able to capture moving, spinning objects
Easily to apply: Motion planning is greatly simplified
Notes: To accomplish this, we use gecko-inspired adhesive grippers
(Key idea)
These can be made from space-qualified materials, and have many advantages over traditional robotic grippers:
  Versatile: Many surfaces are available for grasping, including flat surfaces and curved surfaces, without the need to wrap around an object to pinch it or enclose it in a caging grasp
  Gentle: Shear-activated adhesion can be applied and removed with very little reaction force that might disturb a floating object in microgravity
  Dynamic: Can be used to capture spinning objects, without perfectly grasping a specialized grasping location
  Easily to apply: Widens the envelope for successful grasp, both in terms of grasping locations and tolerance to relative speeds. Makes the goal region for motion planning much larger – for example, can reduce the grasping problem to a docking problem.

## Slide 4: Technical Research Objectives
Objective 1: Design, analyze, and test mechanisms for grasping and manipulation that employ controllable adhesion
Objective 2: Devise control and planning algorithms that allow free-flyers to grasp and manipulate payloads with adhesion-based appendages
Objective 3: Validate the technology on a state-of-the-art test bed at Stanford and on the Astrobee platforms
Notes: So the research objectives of this work on the Astrobee are as follows:
  First is the mechanism design, analysis, and testing of adhesive grippers for assistive free-flyer applications
  Second, making use of the new capabilities of these grippers through new control and planning algorithms
  Third, validating these on state of the art testbeds, both in our lab at Stanford and on Astrobee

## Slide 5: Recent Work: Learning-Based Detection of Grasp Failure
Key contributions:
Machine learning method to detect grasp failure using only onboard sensor data from gripper
Experimental validation of approach on air bearing test bed
Recent experimental setup
Previous work on characterizing dynamic grasping envelopes
Notes: This is a brief update on some very recent work we have been doing
In previous work, we experimental characterized dynamic grasping envelopes
As you might expect, there are many factors that play into whether a dynamic grasp will succeed, including the geometry of the target object, its mass and inertia properties, the magnitude and direction of its linear and angular momentum when it contacts the gripper, etc.
This is quite a lot of parameters to keep track of, and it is actually quite difficult to build a simulation model of the gripper to predict whether a grasp will succeed for an object where we have uncertainty of its parameters.
Thus, when grasping a dynamic object that is not fully characterized, there is some potential that the initial grasp does not fully attach.
- During a grasp, we may want to assess the quality of the grasp and be able to quickly detect when the gripper is not well-attached, allowing us to very quickly make adjustments and attempt a regrasp.
- We want to be able to do so without relying on external data from a visual perception system, since that may be unavailable
So we instead use on-board accelerometers and force/torque sensors and use a support vector machine to be able to quickly detect imperfect grasps

## Slide 6: Recent Work: Learning-Based Detection of Grasp Failure
Notes: - Here is a trial being conducted on our new free-flyer table at Stanford using an adhesive gripper prototype with attached.
In the first case, it successfully grasps
In the second case, the object bounces off the gripper before one of the gripper fully closes, result in an imperfect grasp that the object rolls out of.
  Given early detection, the gripper could conceivably make an adjustment to better secure the object before it slips out
- The paper on the target adds roughness which decreases adhesive capability, making the object much harder to grasp successfully in dynamic situations
- This work is currently under preparation for submission as we collect training data to validate our proposed approach

## Slide 7: Development of Astrobee Adhesive Gripper
Notes: We are also working on integrating a gripper with the Astrobee. This a brief concept video our first application, using the gripper allow Astrobee to perch on a flat wall on the ISSand reorient itself

## Slide 8: Development of Astrobee Flat-Surface Gripper
Notes: This is the most up-to-date version of the Astrobee flat gripper prototype
- The gripper has two pairs of opposed pads, and tendon routing and adhesive pad tensioning is based on previous successful prototypes

## Slide 9: Development of Astrobee Flat-Surface Gripper
Notes: The gripper includes two servo motors
One for applying shear to the adhesive pads to quickly activate or deactivate the adhesion
The other is to change the length of nitinol tendons acting as springs, effectively controlling the compliance of the gripper about its wrist ball joint
This gripper has been sized specifically for the Astrobee and we are currently iterating on prototypes towards the final design.

## Slide 10: Conclusions
Implement and demonstrate adhesive gripper and related planning and control algorithms on assistive free-flyer platforms
Year 1 & 2 – Developed and tested necessary components
Year 3 – Further development, as well as integration and validation
Future: Pursue flight opportunities on Astrobee for ISS deployment and testing in 2019
Notes: To conclude,

## Slide 11: Publications
P. Glick, S.A. Suresh, D. Ruffatto, M.R. Cutkosky, M.T. Tolley, A. Parness, “A soft robotic gripper with gecko-like adhesives” IEEE RA-Letters & ICRA 2018.
J-P Roberge, W. Ruotolo, V. Duchaine, M.R. Cutkosky, “Improving Industrial Grippers with Adhesion-Controlled Friction,” IEEE RA-Letters & ICRA 2018.
A. Bylard, R. MacPherson, B. Hockman, M. R. Cutkosky, and M. Pavone, "Robust capture and deorbit of rocket body debris using controllable dry adhesion." IEEE Aerospace Conference, March 2017.
H. Jiang, E. W. Hawkes, C. Fuller, M. A. Estrada, S. A. Suresh, N. Abcouwer, A. K. Han, S. Wang, C. J. Ploch, A. Parness, M. R. Cutkosky, “A Robotic Device using Gecko-Inspired Adhesives can Grasp and Manipulate Large Objects in Microgravity,” in Science Robotics (AAAS), July 2017.
R. MacPherson, B. Hockman, A. Bylard, M. A. Estrada, M. R. Cutkosky, and M. Pavone, “Trajectory Optimization for Dynamic Grasping in Space using Adhesive Grippers,” Field and Service Robotics, November 2017.
M. A. Estrada, H. Jiang, B. Noll, E. W. Hawkes, M. Pavone, and M. R. Cutkosky, “Force and moment constraints of a curved surface gripper and wrist for assistive free flyers,” in Proc. IEEE Conf. on Robotics and Automation, 2017.
M. A. Estrada, B. Hockman, A. Bylard, E. W. Hawkes, M. R. Cutkosky, and M. Pavone, “Free-flyer acquisition of spinning objects with gecko-inspired adhesives,” in Proc. IEEE Conf. on Robotics and Automation, 2016.

## Slide 12: Experimental Validation Onboard the ISS
Task/Experiment | Ground Testing Period
Real-time planning for short-range free-flying navigation with obstacle avoidance | Fall 2017-Summer 2018
Integration of a gecko-inspired adhesive gripper and planning and control for grasping | Fall 2017-Summer 2018
Planning for free-flying and free-floating payload manipulation | Spring-Summer 2018
High-level planning algorithm for long-range navigation | Fall 2018 (sim only)

## Slide 13: Current State of the Art
Capturing the Wester 6 satellite
Traditional spacecraft docking and robotic manipulators
Requires complex, time-consuming procedures for maneuvering, alignment, docking
Often need specialized docking or grasping features
Difficult to capture moving, spinning objects
ISS Canadarm during resupply
NASA Docking System

## Slide 14: Experimental Validation Onboard the ISS
Task/Experiment | Ground Testing Period | Proposed ISS Test Period
Real-time planning for short-range free-flying navigation with obstacle avoidance | Fall 2017-Summer 2018 | Winter 2019 onwards
Integration of a gecko-inspired adhesive gripper and planning and control for grasping | Fall 2017-Summer 2018 | 
Planning for free-flying and free-floating payload manipulation | Spring-Summer 2018 | 
High-level planning algorithm for long-range navigation | Fall 2018 (sim only) |