## Slide 1
RFID-Enabled Autonomous Logistics Management
(REALM)
Status 2/28/18
(update from 11/30/17)

## Slide 2: REALM-2: RFID Recon
Concept: Astrobee equipped with RFID reader and antennas is used to conduct autonomous inventories and searches
REALM-2 is an experimental payload module that attaches to the front bottom payload bay of Astrobee
Objective 1: expand RFID coverage area, both in REALM-1 instrumented and non-instrumented modules
  example: can provide another mobile coverage zone during logistics activities
Objective 2: refine item location beyond REALM-1 capability
  Additional CEP context for REALM-1 localization engines on ground
  Homing on specific tag
Astrobee/REALM-2 Early Integration Test – 6/24/16

## Slide 3: REALM-2: status
    REALM-2 is now an official ISS payload
    Completed EMI Radiated Emission (RE02) engineering evaluation
    Acoustics test scheduled for March 14.

## Slide 4: Backup

## Slide 5: REALM-2 Con-Ops: Missions
Astrobee Docking Station
JSL
HOSC
REALM-2
Control Station
CEP System
Mission
File
- Contains Block Types
*Hooks only - not currently in scope
IMS Clone
REALM-2 Mission Types
A - Teleoperation
B – Inventory
C – Tag Search
D – Ad hoc fixed reader
E – Map REALM-1 fields
F – RFID Sensing*
G – 6-DoF WHISPER System*

## Slide 6: Schedule