## Slide 1
RFID-Enabled Autonomous Logistics Management
(REALM)
Status 6/19/18
(update from 2/28/18)

## Slide 2: REALM-2: RFID Recon
Concept: Astrobee equipped with RFID reader and antennas is used to conduct autonomous inventories and searches
REALM-2 is an experimental payload module that attaches to the front bottom payload bay of Astrobee
Objective 1: expand RFID coverage area, both in REALM-1 instrumented and non-instrumented modules
  example: can provide another mobile coverage zone during logistics activities
Objective 2: refine item location beyond REALM-1 capability
  Additional CEP context for REALM-1 localization engines on ground
  Homing on specific tag

## Slide 3: REALM-2: Hardware
RFID Recon Hardware has three project-supplied components:
  Main Module (qty 1) - RFID reader with two installed antennas
  E-textile Antenna Astrobee Skin Assembly (qty 2)
    Textile antenna fabricated and embedded into Astrobee Propulsion Module skin by JSC Softgoods Lab
    Assembly includes COTS RF coaxial cable
  SD Card (qty 1) - Used for OS and data storage onboard Reader

## Slide 4: REALM-2: Status
    Performed basic integration test with Astrobee flat sat
      Lever lock to clevis
      Power up with Astrobee battery and comm with HLP
    Held System Requirements Review and System Design Review
    Participate with Payload Safety Review Panel phase I/II
      Need to finalize grounding and bonding strategy
      Need to verify no exceedance of 45 deg C touch temperature
    Met with Human Factors Implementation Team
    Looking at routing of coaxial cable from main module to propulsion module antennas
REALM-2 prototype integrated with Astrobee flat sat – March 2018

## Slide 5: Backup

## Slide 6: REALM-2 Con-Ops: Missions
Astrobee Docking Station
JSL
HOSC
REALM-2
Control Station
CEP System
Mission
File
- Contains Block Types
*Hooks only - not currently in scope
IMS Clone
REALM-2 Mission Types
A - Teleoperation
B – Inventory
C – Tag Search
D – Ad hoc fixed reader
E – Map REALM-1 fields
F – RFID Sensing*
G – 6-DoF WHISPER System*

## Slide 7: REALM-1: Logistics Awareness Overview
1st Goal: localize tagged cargo with ½-module resolution or better using fixed RFID coverage zones
  Element modules are ~ 3.5m diameter and vary 5.5-8.5m in length
6 fixed RFID readers and 24 antennas in 3 modules
3 instrumented modules for experimental phase: N1, USL, N2
  Primary pathway for cargo translation following offload of visiting vehicle
Data is downlinked to the ground for archival, mining, and Complex Event Processing (CEP)
downlink
~430 CTBE/yr
PMA-3
N2
COL
JPM
JLP
LAB
N3
N1
A/L
ФГБ
PMA-1
Z1
FGB
PMA-2
PMM

## Slide 8: REALM-1 On-Orbit Pic: Node 2 Port Reader
Antenna looking into Node 2 end cone (nadir )
Antenna looking into Columbus (nadir)