## Slide 1: MagTags™ Modular Servicing Interface Overview
Altius Space Machines, Inc.
Jonathan Goff | President/CEO | jongoff@altius-space.com | 801-362-2310

## Slide 2: Why MagTags? (Satellite Applications)
Extend life by refueling and installation of modular replacement parts
Avoid technology obsolescence via modular upgrades
Enhance business flexibility via on-orbit swap-out of hosted payloads
Enable persistent platforms via plug and play modules for assemblies and upgrades
Altius Space Machines, Inc.
Jonathan Goff | President/CEO | jongoff@altius-space.com | 801-362-2310

## Slide 3: Why MagTags? (ISS/Gateway/Comm’l Habitat Applications)
Low-profile robotically installable hosted payload interface (internal or external)
Low-profile ORU interface for modularly interchangeable internal/external components
Modularly repairable life support systems/consumable canister interfaces
Grappling point for robotic outfitting panel manipulation
Low-profile power/data anchor point for internal robotics
Altius Space Machines, Inc.
Jonathan Goff | President/CEO | jongoff@altius-space.com | 801-362-2310

## Slide 4: MagTags Modular Interface
“USB Ports” for satellites
Low profile
  75mm x 75mm x 15-25mm
  75g target for passive half
  <150g target for active half
Switchable magnetic latching with 300-400N magnetic gripping force
Active/Passive Interface design
  Passive interface on customer spacecraft
  Active interface on installed modules
Ground interchangeable central core element to enable different MagTag types
Altius Space Machines, Inc.
Jonathan Goff | President/CEO | jongoff@altius-space.com | 801-362-2310
Active Side
Passive Side
MagTag Core Element
(power/data version shown)
Switchable Magnets
Alignment/Power
Pins/Sockets
Ferrous Gripping Surfaces

## Slide 5: Configurable Cores Enable Many Types of MagTags
Potential MagTag core types:
  Power/Data
  Fiber optic
  Low-pressure liquid transfer (Water, etc)
  Low-to-high pressure gas transfer (Xenon, Helium, Oxygen, Nitrogen, etc)
  Motorized rotary drives
  Motorized linear drives/solenoids
  No fluid-transfer heat transfer connections
  Adapters to other interface standards (HiSats, etc.)
  Combination cores (fluid + electrical, dual-fluid, etc)
  Etc.
Potential MagTag-enabled plug and play modules:
  Swappable hosted payloads
  Battery extender
  Reaction wheel replacements
  Laser comms upgrades
  Avionics upgrades/backups
  Sensor modules
  Solar array + rotary drive
  Expendable refueling tank
  Hall Effect Thruster replacement
  Etc.
Altius Space Machines, Inc.
Jonathan Goff | President/CEO | jongoff@altius-space.com | 801-362-2310

## Slide 6: MagTags Progress
Pre-Alpha prototype built and demoed at USU Smallsat Conference in early Aug 2018
  Successful workshop held with 54 participants
NASA SBIR Phase I for MagTags started in early Aug 2018
  Focused on power/data version of DogTags
AFRL SBIR Phase I for MagTags awarded in Sep 2018
  Customer discovery for other core types
  Proof of concept demo of Xenon transfer core
Alpha prototype built and delivered to Orbitfab in Sep 2018 for ISS qualification and flight-demo
  Passed EMI/EMC tests at MSFC during week of 9/24/2018
  Planned to launch on CRS-16 in Dec 2018
Altius Space Machines, Inc.
Jonathan Goff | President/CEO | jongoff@altius-space.com | 801-362-2310

## Slide 7: MagTag Early Access Program
$15k participation fee
Participants receive a prototype active/passive coupling pair for each of three generations of MagTag:
  “Alpha” version – based on lessons learned from the “pre-alpha” version developed for the USU SmallSat conference. Available late Oct/Nov 2018
  “Beta” version – based on feedback from customers and a NASA SBIR Phase I effort (July 2018-Jan 2019). Available Feb/Mar 2019.
  Flight-qualified MagTag hardware – including vibe, thermal-vac and EMC qualification testing. Available late 2019/early 2020.
Program to provide interested customers with early MagTag prototypes to experiment with
  Enhances feedback to Altius to guarantee MagTag compatibility with your system
  Early prototypes to enable integration work with your spacecraft HW/SW
  Early prototypes to allow customers to develop their own cores or work with Altius to develop custom cores for different applications
Altius Space Machines, Inc.
Jonathan Goff | President/CEO | jongoff@altius-space.com | 801-362-2310

## Slide 8: Contact Information
Jonathan Goff (CEO)
jongoff@altius-space.com
801-362-2310
Joshua Nelson (PI)
nelsonj@altius-space.com
303-913-4387