## Slide 1: Assistive Free-Flyers with Gecko-Inspired Grippers for Automated Logistics in Space
Mark Cutkosky
Biomimetics and Dextrous Manipulation Lab
Department of Mechanical Engineering
cutkosky@stanford.edu
Marco Pavone
Autonomous Systems Laboratory
Department of Aeronautics and Astronautics
pavone@stanford.edu
October 3, 2018

## Slide 2: Payload Summary
Research Goal:
Integrate adhesion-based grasping with adhesive robots to enable them to grasp and manipulate payloads and perch on walls in a microgravity space environment
Key Investigation Objectives:
Integrate a flat-surface gecko-inspired adhesive gripper with the Astrobee robot on the ISS
Test the capabilities of the gripper for manual and autonomous perching of the robot onto the ISS walls and other flat surfaces

## Slide 3: Technical Research Objectives
Objective 1: Design, analyze, and test mechanisms for grasping and manipulation that employ controllable adhesion
Objective 2: Devise control and planning algorithms that allow free-flyers to grasp and manipulate payloads with adhesion-based appendages
Objective 3: Validate the technology on a state-of-the-art test bed at Stanford and on the Astrobee platforms
Notes: So the research objectives of this work on the Astrobee are as follows:
  First is the mechanism design, analysis, and testing of adhesive grippers for assistive free-flyer applications
  Second, making use of the new capabilities of these grippers through new control and planning algorithms
  Third, validating these on state of the art testbeds, both in our lab at Stanford and on Astrobee

## Slide 4: Integration with Astrobee Arm
Fits within the stowage packaging of Astrobee gripper
Overall planar size 3.7” by 3.77”
Interfaces with Astrobee arm through 6 captive screws in the interface plate

## Slide 5: Integration with Astrobee Arm
Fits within the stowage packaging of Astrobee gripper
Overall planar size 3.7” by 3.77”
Interfaces with Astrobee arm through 6 captive screws in the interface plate

## Slide 6: Engineering Unit
2 servos control 2 different load tendons, one for each pair of adhesive tiles
1 servo control all the release tendons
Passive locking wrist provides ~7.5° compliance in all rotational directions
1 servo controls 3 pairs of tendons to lock pitch, roll and yaw DoF when activated

## Slide 7: Engineering Unit

## Slide 8: On-Board Electronics
Two custom designed PCB integrating all the circuits needed onboard
4 lines connecting the top and bottom PCB

## Slide 9: On-Board Electronics
Teensy 3.2 Microcontroller
INA219 High Side DC Current Sensor
PCA9685 12-bit I2C Servo Driver
VL6180X Time-of-Flight Sensor
https://www.pjrc.com/teensy/teensy31.html

## Slide 10: Recent Work
Sequential convex optimization for free-flyer trajectory generation
  Extends previous work by providing convergence guarantees
Notes: -- Convex optimization
This is a brief update on some very recent work we have been doing
This quarter, we implemented our recent sequential convex programming (SCP) algorithm GuSTO
SCP is a framework capable of generating collision-free trajectories in real time while satisfying dynamics and actuator constraints
We implemented GuSTO on the Stanford free-flyer testbed (start video here

## Slide 11: Preliminary Schedule
Active Dates | Activities | Deliverables
April 23, 2018 | Systems Requirements Review | Document of known systems requirements
July 2018 | Preliminary Design Review | First iteration of monolithic 3D-printed gripper prototype
August 2018 | Critical Design Review | (1) Updated gripper design to meet safety and operational requirements, (2) Initial safety and operational documentation
Sept. 2018 | Systems Integration Review | Intended final gripper design and manufacture
Oct. 2018 | Operational Readiness Review | (1) Flight-ready gripper and other payload elements, (2) Additional documentation to prepare for flight experiments
Dec. 2018 | Flight Readiness Review | Finalized payload and documentation
April 2019 | Launch | 
April-Sept. 2019 | ISS Experiments | 

## Slide 12: Conclusions
Implement and demonstrate award-winning STMD technologies on assistive free-flyer platforms
Year 1 & 2 – Developed and tested necessary components
Years 3 – Integration and validation
Future: Pursue flight opportunities on Astrobee for ISS deployment and testing in 2019

## Slide 13: Publications
P. Glick, S.A. Suresh, D. Ruffatto, M.R. Cutkosky, M.T. Tolley, A. Parness, “A soft robotic gripper with gecko-like adhesives” IEEE RA-Letters & ICRA 2018.
J-P Roberge, W. Ruotolo, V. Duchaine, M.R. Cutkosky, “Improving Industrial Grippers with Adhesion-Controlled Friction,” IEEE RA-Letters & ICRA 2018.
A. Bylard, R. MacPherson, B. Hockman, M. R. Cutkosky, and M. Pavone, "Robust capture and deorbit of rocket body debris using controllable dry adhesion." IEEE Aerospace Conference, March 2017.
H. Jiang, E. W. Hawkes, C. Fuller, M. A. Estrada, S. A. Suresh, N. Abcouwer, A. K. Han, S. Wang, C. J. Ploch, A. Parness, M. R. Cutkosky, “A Robotic Device using Gecko-Inspired Adhesives can Grasp and Manipulate Large Objects in Microgravity,” in Science Robotics (AAAS), July 2017.
R. MacPherson, B. Hockman, A. Bylard, M. A. Estrada, M. R. Cutkosky, and M. Pavone, “Trajectory Optimization for Dynamic Grasping in Space using Adhesive Grippers,” Field and Service Robotics, November 2017.
M. A. Estrada, H. Jiang, B. Noll, E. W. Hawkes, M. Pavone, and M. R. Cutkosky, “Force and moment constraints of a curved surface gripper and wrist for assistive free flyers,” in Proc. IEEE Conf. on Robotics and Automation, 2017.
M. A. Estrada, B. Hockman, A. Bylard, E. W. Hawkes, M. R. Cutkosky, and M. Pavone, “Free-flyer acquisition of spinning objects with gecko-inspired adhesives,” in Proc. IEEE Conf. on Robotics and Automation, 2016.
A. Cauligi, A. Bylard, R. Bonalli, and M. Pavone, “A Sequential Convex Programming Approach for Free-Flying Robot Trajectory Generation,” in Int. Symp. On Artificial Intelligence, Robotics and Automation in Space, 2018.
R. Bonalli, A. Cauligi, A. Bylard, and M. Pavone, “Sequential Convex Programming: Generalized Method and Theoretical Convergence Guarantees for Trajectory Optimization,” in Proc. IEEE Conf. on Robotics and Automation, 2018 (submitted).