## Slide 1
7/8/2021
REALM-2 Project
Radio Frequency Identification (RFID) Reconnaissance (Recon) Payload
Notes: <number>

## Slide 2: Experiment Overview
RFID Recon is an RFID reader that is installed in the bottom forward payload bay of Astrobee. It is the second phase of the REALM (RFID Enabled Autonomous Logistics Management) project. Phase one of REALM (REALM-1) is RFID Logistics - a fixed RFID system on ISS located in Node 1, USL, and Node 2 that has been operational since Feb 2017.
Primary objectives of RFID Recon:
  – Expand RFID coverage to RFID Logistics non-instrumented modules, as well as nulls in instrumented modules
  – Refine localization estimates
    Additional Complex Event Processing (CEP) context for RFID Logistics localization engines on ground (i.e., additional fixed reader)
    Search for a specific tag
Onboard ISS in Nov 2019 (NG-12)
July 8, 2021
SPHERES/Astrobee WG
<number>

## Slide 3: RFID Recon Installed on Astrobee
Propulsion Module Antenna embedded in left and right skins
RFID reader with 2 antennas
July 8, 2021
SPHERES/Astrobee WG
<number>

## Slide 4: Accomplishments
July 8, 2021
SPHERES/Astrobee WG
<number>
Commissioned with Astrobee in JPM on 1/29/21
Tested basic functionalities:
  Able to read RFID tags (read 35 unique items)
  Can move Astrobee along waypoints
  Verify that we will not transmit in implemented Quiet Zone
  Home in on a Cargo Transfer Bag (CTB) placed in front of Astrobee
ISAAC – participation on 3 mapping missions 2/23/21, 3/26/21, 4/19/21
ISAAC-1 – read 129 unique items
ISAAC-2 – read 166 unique items
ISAAC-3 – read 248 unique items

## Slide 5: Near Term Plans
RFID Recon Science-1 mission
  Crew to translate Astrobee to PMM and perch Astrobee at PMM hatch on Multi-Use Bracket
  Read RFID tags in PMM while perched (a storage location on ISS)
  ECR is completed and crew procedure baselined
  Need to address CHIT with MER concerning possible interference
Planning RFID Recon Science-2 mission
  Perform homing missions in JPM to expand on basic homing mission during commissioning
    Perform rotation for cases where Astrobee is not already facing target
    Sortie in which Astrobee has to locate the target before homing into target
July 8, 2021
SPHERES/Astrobee WG
<number>

## Slide 6
Backup
July 8, 2021
SPHERES/Astrobee WG
<number>

## Slide 7: RFID Recon Reader Module
Antennas (2)
Fans (2)
Connections to Propulsion Module antennas (2)
Magnets (4)
SD card slot
Reader mounted antennas (2)
Fans (2)
Connections to Propulsion Module antennas (2)
SD card slot
July 8, 2021
SPHERES/Astrobee WG
<number>

## Slide 8: Propulsion Module Antenna Bumble Skins
July 8, 2021
SPHERES/Astrobee WG
<number>

## Slide 9: REALM-1: RFID Logistics Awareness Overview
1st Goal: localize tagged cargo with ½-module resolution or better using fixed RFID coverage zones
  Element modules are ~ 3.5m diameter and vary 5.5-8.5m in length
6 fixed RFID readers and 24 antennas in 3 modules
3 instrumented modules for experimental phase: N1, USL, N2
  Primary pathway for cargo translation following offload of visiting vehicle
Data is downlinked to the ground for archival, mining, and Complex Event Processing (CEP)
downlink
~430 CTBE/yr
PMA-3
N2
COL
JPM
JLP
LAB
N3
N1
A/L
ФГБ
PMA-1
Z1
FGB
PMA-2
PMM
July 8, 2021
SPHERES/Astrobee WG
<number>
Notes: <number>

## Slide 10: RFID Recon Con-Ops: Missions
Astrobee Docking Station
JSL
HOSC
RFID Recon
Control Station
CEP System
Mission
Package
RFID Recon Mission Types
A - Teleoperation
B – Perched Astrobee
C – Inventory
D – Tag Search
E – CEP Context
F – Map RFID Logistics fields
G – RFID Sensing*
H – 6-DoF WHISPER System*
*Hooks only - not currently in scope
IMS Clone
Autonomous
July 8, 2021
SPHERES/Astrobee WG
<number>