## Slide 1: Astrobee A-smels Automated System for Monitoring Environmental Life Support SPEC Sensors LLC. | Autonomous Environmental Monitoring and Management Platform for Remote Habitats
Dr. David Peaslee, PI at SPEC Sensors LLC
Collaborators:
Ted Tagami, Magnitude.io
Drs. Mtibaa and Adhikari of the Department of Math and Computer Science at the University of Missouri – St. Louis
KWJ Engineering, Inc.
NASA STTR Grant #G80NSSC20C0316

## Slide 2: Designed to meet NASA Goals for Remote Habitat Management
Missions on the moon or Mars will benefit from this lightweight, low power, AI enabled AQ platform to ensure safety in vehicles, airlocks, and portable life support systems.
This will provide tools necessary to measure the quality of air in a habitat, and to identify and locate potential hazards in a closed environment.
  Electrical shorts can be detected with the localization of an ozone source
  A potential fire can be identified before a combustion event with the detection of soot, carbon monoxide, and other flammable gasses.

## Slide 3: Designed to meet NASA Goals for Remote Habitat Management
Tasks to meet these goals:
  Develop a payload capable of monitoring environmental air quality (AQ) while onboard a flee flying robot such as Astrobee
  Develop AI algorithms to
    Map the environments normal sources of gas, i.e., ozone from electronics, body odors in areas of exercise.
    Identify chemistry of gas and potential sources, i.e., electrical shorts
    Localize the source, use machine learning to generate shortest path to source of gas.
  Develop an interface to remotely sample scientific payloads and sealed areas while onboard a robotic caretaker.
  Network AQ monitors to simplify monitoring and calibration routines

## Slide 4: A-SMELS Design
Magnitude Developing a Universal Payload Enclosure to incorporate standardized PCB (PC104 3.550” × 3.775”)
SPEC Developing a 3 Gas sensor in Adafruit Feather Formfactor (0.9”x2.0”)
  2 Electrochemical sensors, 1 T/P/Rh/VOC Sensor
  Up to 4 sets per payload.

## Slide 5: A-SMELS Design: Sensor Selection
  Up to 4 dual sensor with onboard BME680
    3.3V: I2C1 (or 4th on UART0 bus)
  Light sensor SiLabs SI1145
    3.3V: I2C1
  Accel. Bosch BMA456
    3.3V: I2C1
  2x Sensirion SPS30
    5V UART
  CO2 Sensirion SCD40
    3.3 I2C1 or 5.5V I2C2
H: 3.550” L: 3.775”
H
L
Overhang is ½” for connectors
I2C2 or UART2 for GPS
I2C1
I2C1
I2C1
AB-Power
AB-USB
UC
3 Ana Input 3V
UART1
UART2
SCD40 CO2
EEPROM
ACCEL/ GYRO
5V Boost
Light
Power
Need Border for Flow Cell Control

## Slide 6: A-SMELS Design: Board Layout

## Slide 7: A-SMELS Design: Board Layout
Flow Cell:
  Printable, with flexible material for gaskets
  Flexible, detachable proboscis for hard to reach places
Next versions for science payload interface
  Need to dock to standardized gas ports of hermetic payload enclosures

## Slide 8: A-SMELS Operation
Phase I: Passive Monitoring
  Develop 3D Training Data Set
  Will ride along in pre-planned flights
Phase II: Localization
  Identify sources of gas/odor, i.e., body or food odors.
Phase III: Automation
  Calibration Routines
  Equipment Monitoring

## Slide 9: Alternative Use for Lower Cost Educational Platform
Need ruggedized equivalent version for classrooms for AQ studies
Can be modified for standalone versions for stationary monitoring
  Wildfire detection
  Confined space monitoring
  Wearable monitoring
H: 3.550” L: 3.775”
H
L
Overhang is ½” for connectors. Will have to work out if it goes in top or bottom edge.
Has Micro and Lipo battery circuit. Can provide 5V and 3V bus when connected to USB
I2C1
I2C1
I2C1
I2C1/5V
I2C2/5V
SCD40 CO2
5V Boost
Power
Need Border for Flow Cell Control, ideally fit SCD40 within the flow cell
Gyro
Light
Power control, allow for pin input of 5-18 V DC, step down to 5 and 3. Bypass-able when power supplied by Micro module or USB input. Boost when only 3.3 V supplied by Micro module
UART 5V

## Slide 10: Astrobee A-SMELS Automated System for Monitoring Environmental Life Support
Next Steps
Research & Design
  3D Rig for environmental mapping of sources for ground based training data set
  Work with scientific payload designers for interoperability
Approvals
  Apply for Official Payload Status
  Materials Approval
  System Checkout
Seeking Further Funding
  NASA STTR Phase II
  National Labs
Hurdles
Requires Continuous Power
Approved materials selection
Interfacing with Astrobee