## Slide 1: Vision-Based Navigation for Formation Flight on ISS
July 8, 2021
Hector Gutierrez
Florida institute of technology - aerospace systems and propulsion lab
Jiten chandiramani
Jaycon systems, LLC

## Slide 2: RINGS – SVGS: STTR Phase II – Objectives
1. Integration of Astrobee + SVGS
(i) deployment of SVGS on HLP (using guest science camera)
(ii) SVGS Mission APK
2. Electromagnetic Propulsion Assist (EPA) using RINGS
(i) correction of hardware and firmware issues in RINGS
(ii) Electromagnetic Propulsion Assist using RINGS
(iii) experimental demonstration of EPA : 3DOF ground experiment
3. SVGS Deployment on ISS
(i) Development and HIL of ISS science sessions for SVGS-Astrobee
(ii) SVGS Payload development / Ground testing / Safety Review/ EMC /POWR
4. SVGS Science Mission on ISS

## Slide 3: Outline – Q9
      1. Completion of RINGS Objectives
      Modifications to RINGS hardware to resolve issues identified during ISS Mission
      Completion of 3DOF motion ground control platform for RINGS
      Demonstration of Electromagnetic Propulsion Assist (EPA) using RINGS
        3DOF EM motion control based on Near Field models
      2. Software Integration of SVGS and Astrobee
      3. Hardware Integration: SVGS Payload and SVGS Mission

## Slide 4: Electromagnetic Formation Flight
  MIT-SSL: Relative position control of satellite array by EM actuation using magnetic dipoles
(Sedwick, Kwon, Lee, & Ramirez-Riberos, 2011)
RINGS: UMD, MIT:
Electromagnetic Formation Flight
Wireless power transfer (WPT)
ISS Science Sessions:
Science 1 (Aug. 2013) | Open-loop electromagnetic tests for model validation
Science 2 (Feb. 2014) | Axial closed-loop electromagnetic tests
Science 3 (July, 2014) | Additional model validation tests, Axial closed-loop electromagnetic tests
(Hilton, 2015)
  Each vehicle has:
    Two orthogonal coils
    A reaction wheel
  Demonstrated EMFF maneuvers

## Slide 5: Assessment of RINGS
Problems found:
Estimator issues (lack of convergence)
Thruster impingement
RINGS firmware issues (communications)
Loss of synchronization
RINGS Testbed at FIT:
Motion platform developed for RINGS ground testing
Formation flight using SVGS as position/attitude sensor
Motion control via ducted fans
EMFF axial control maneuver
(Avendaño, 2015)
(Hariri, 2018)

## Slide 6: RINGS – Loss of Synchronization
Loss of synchronization caused by floating SD pin in IR circuitry (TFDU4101)
SD pin tripped by changing EM fields generated by RINGS
Result in unpredictable behavior during maneuvers
Old IR PCB
New IR PCB
Proposed solution: New IR PCB w/ SD tied to GND
Successful resolution of IR SD pin issue
IR Daisy Chain unreliable: (i) poor connections, (ii) false positives form stray IR light sources
5-min Test
Synchronization
Pulse
IR connector in RINGS:

## Slide 7: RINGS Synchronization RF Solution
IR daisy chain replaced with an RF transmitter/receiver
RF modules ping each other and simultaneously send a synchronization signal
RINGS Microcontroller is opto-isolated from RF module
Synchronization
Pulse
Opto-isolation Circuit
NRF24L01 Microcontroller
RINGS Synchronization Signal Port

## Slide 8: Platform Revision: Phase II
Phase I Version
Phase II Version
3DOF RINGS Ground Motion Platform was redesigned and rebuilt to improve reliability
Motion Platform Mounting Frame

## Slide 9: 3DOF Motion Platform Revision: Electronics
Dedicated PCB designed to replace separate breadboards and jumper wires
All electronics integrated into one PCB
Phase I Electronics
Phase II Motion Platform PCB Layout

## Slide 10: RINGS 3DOF Motion Control Platform for Ground Testing – Phase II

## Slide 11: RINGS Firmware Analysis and Firmware Revisions
Motion Platform was designed to communicate with RINGS firmware version 9.4
Analysis of later versions revealed significant communications errors
Error handler reintroduced into version 9.4
11.4 Firmware vs 9.4
= missing from 9.4

## Slide 12: 3DOF Motion Vehicle Dynamics System Identification
Rotational Dynamics:
Translational Dynamics:
State Vector:
Where,
  Fan Force:
  Fan Torque:
  Friction force: N
  0.3742 Iz 0.5344 kg m2
Fitting percentages:
Gray-box model estimates:
State Space model equations:

## Slide 13: System Identification and State Estimation

## Slide 14: 3DOF Motion Stage Ducted Fan Control using LQG Servo
Quadratic cost function:
State vector weighting matrix:
Control output weighting matrix:
LQR:
LQG-servo:
LQ-servo control law:
State-space model :
Cost function :
Kalman Filter design and integration:
Sensor Noise:
Process Noise:
SVGS sensor does not return full state vector
Notes: 𝚺 = measurement noise covariance matrix
𝚵 = process noise covariance matrix

## Slide 15: 3DOF LQ Servo Control with SVGS feedback

## Slide 16: Modeling EM Forces and Torques between RINGS
3DoF Far-Field Forces/Torques:
Coaxially Aligned Simplification
Points Source EM Dipoles
Geometry of two coil far-field model
Magnetic Moments
Near-field interaction between coil segments
Biot-Savart Law
Far-Field Model
Near-Field Model
Near-field Forces and Torque Equations
Near-field Force: Discrete Current Segments

## Slide 17: Reduction of thruster power consumption using Electromagnetic force assist
It seems at first that RINGS can only provide actuation in a limited sense: only amplitude and sign (phase) of currents can be controlled
But Magnetic Field has 3D components that can be controlled for actuation, one axis at a time
 New vision for electromagnetic actuation in spacecraft: reduction of thruster power consumption by using electromagnetic force assist
3DOF Control with Near-Field force and torque models:

## Slide 18: 3DOF Near-Field Force and Torque models
Examples of polynomial approximation surfaces of Force Fx, Force Fy, Torque Tz
Magnetic Forces between two coils [Hilton, et al., 2013]:

## Slide 19: Electromagnetic assist using SMC + Feed Forward Controller
Feed-forward control is based on a-priori knowledge: near-field force/torque as function of 3DOF position
FFC controller: theoretical control current to achieve a desired position
Feedback action compensates model error and parametric uncertainties
1DOF is controlled by , other 2DOFs are regulated by LQG-servo controller
Example : FFC + SMC for electromagnetic rotation control + LQG-servo for 2DOF translation motion control in X,Y

## Slide 20: RINGS EM Control: Feedforward + Sliding Mode Method
Polynomial Approximations of Near-Field model (1 DoF Each):
Model Inversion of Rotational Dynamics Case:
Example: SMC control of rotation using electromagnetic assist + LQG-servo for 2-axis translation motion control
To perform 3DOF motion, maneuvers are separated in single-axis components. Each segment controls one DOF with input current i2 from SMC (i1= Imax) and thrusters (controlled by LQG-servo) regulate other 2 DOFs

## Slide 21: EM Assist Maneuvers – Power Consumption Savings
EM maneuver power savings for LQG-servo
Power consumption savings are estimated as the integral of LQG-servo control effort over duration of test
Power savings depend on selection of waypoints (trajectory)
EM maneuvers list w/ set points

## Slide 22: 3 DoF Simulated Maneuvers: LQG-servo + Feedforward + Sliding Mode
Maneuver 3
Maneuver 5
Maneuver 6

## Slide 23: Experimental Demonstration of Electromagnetic Thrust Assist
SVGS Phone Sensor
USB-C for remote screen interface
SVGS Target
Motion Vehicle
Stationary Vehicle

## Slide 24: EM Assist Maneuver: Axial force as function of x for fixed angular position and fixed y

## Slide 25: EM Assist Maneuver: Axial Motion Case
Design Parameters:
{λ, , φ} = {0.3, 0.04, 0.005}
Power Savings:
3%

## Slide 26: EM Assist Maneuver: Shear force as function of y for fixed angular position and fixed x

## Slide 27: EM Assist Maneuver: Shear Motion Case
Design Parameters:
{λ, , φ} = {0.3, 0.04, 0.005}
Power Savings:
20%

## Slide 28: EM Assist Maneuver: Torque as function of θ for fixed x and y

## Slide 29: EM Assist Maneuver: Controlled Rotation Case
Design Parameters:
{λ, , φ} = {0.3, 0.04, 0.005}
Power Savings:
60%

## Slide 30: Conclusions and Future Work
A novel method has been proposed to perform Electromagnetic Thrust assist leading to potential savings compared to pure thruster actuation
The method uses polynomial approximations of the near-field EM forces and torques and both feedforward and nonlinear control
Previously existing approaches for EM-based motion control:
  Based on far-field approximations
  Achieve control by using a separate coil for each DOF
EM actuation assist in 3 independent DOFs has been demonstrated using axial, shear, and rotation motion control cases
% power savings depends on trajectory and needs to be optimized

## Slide 31: Electromagnetic Actuation for Satellite Formation Flight
Motivation:
  Enable more complex space missions
  Lower total cost and risk
  Wider resolution and range
    (e.g.: AFRL: TechSat 21 program)
Challenge:
  Consumable propellant needed for flight formation control
Alternative:
  Electromagnetic Formation Flight:
    Propellant-free reorientation
    Longer service life
    Higher reliability
TechSat21: (Burns, McLaughlin, Leitner, & Martin, 2000)
(Coulter, 2003)
(Martin, Klupar, Kilberg, & Winter, 2001)

## Slide 32: SVGS: Smartphone Video Guidance Sensor
Object and Camera Frame Geometry in SVGS
Smartphone flash illuminates reflective targets on target spacecraft
Capture image of illuminated targets
6-DOF state extracted from 2D image based on geometry

## Slide 33: SVGS Mission Objectives
Main Objectives:
Demonstrate SVGS as position-attitude sensor that can be deployed using Astrobee’s hardware resources. Astrobee will be used to conduct a set of maneuvers while reading 6DOF position/attitude vector from SVGS
Assess SVGS performance in proximity maneuvers on ISS:
  SVGS readings will be stored in Astrobee’s HLP and will be used two ways:
    In stand-alone maneuvers, SVGS readings will be compared to Astrobee metrology to benchmark position/attitude performance
    In formation flight maneuvers, performance using SVGS readings as waypoint commands will be compared to synchronized flight using Astrobee’s native metrology
Optional Objective
Integration of SVGS with Astrobee’s State Estimator (Localization Pipe) :
assess performance of SVGS as position/attitude sensor for Astrobee by sensor fusion

## Slide 34: SVGS Payload Overview
SVGS payload is a 4-point illuminated target for the SVGS app running on Astrobee’s HLP
Main features:
  Electrical: SVGS payload includes 4 LEDs, a DC-DC converter, a LiPo battery, and a dimmer
  Batteries: Payload uses same batteries as Astrobee but has no electrical connection to it
  Mechanical: SVGS payload can be mounted on Astrobee’s payload bay, or be attached to ISS walls using seat tracks and seat track extenders
  Software: SVGS mission APK deployed in Astrobee’s Guest Scientist Platform (HLP)
  CONOPS:
    SVGS payload is attached depending on maneuver to be implemented
    SVGS maneuvers and data acquisition controlled by SVGS Mission APK
    After setting SVGS payloads as needed, SVGS mission app runs from GDS
    Data collected during maneuver: SVGS data, Astrobee kinematics data, time stamps
    Data for each maneuver stored on file on HLP and later downloaded

## Slide 35: SVGS Payload- Rev 7
SVGS payload uses M561payload interface
Bungee cord retention for battery
Includes battery over-discharge protection circuit
EM shield changed to Mu-metal foil
Material: ULTEM 9085

## Slide 36: SVGS Payload – Rev 7

## Slide 37: Electrical Interconnection Diagram
SVGS Payload does not have any electrical or data connections
with either Astrobee or ISS
SVGS payload is powered by ND2054HD34 Astrobee battery:
  Includes over-discharge protection circuit
  DC DC converter
  Dimmer to control LED intensity
  Electronics are shielded with mu-metal to minimize EMI

## Slide 38: SVGS Payload - ISS Wall Mounting
SVGS payload mounted on ISS panel rail using a Handrail Extender to lock into a seat track

## Slide 39: SVGS Payload - ISS Wall Mounting
SVGS payload – wall mounting example using Handrail Extenders. Maneuver 3 and 4 (Slides 50, 51)

## Slide 40
Software Integration of Astrobee - SVGS
40
HLP Guest Science APK: SVGS Mission APK
GDS will be used to start and configure SVGS Mission APK
    SVGS Mission APK:
      Uses images from Sci Cam
      Calculates target’s 6DOF position/attitude vector at 20 Hz
      Saves to file on HLP: SVGS 6-DOF vector, Astrobee kinematics vector, and time stamps, at 20 Hz
    In formation flight maneuvers, SVGS Mission APK uses Astrobee’s Mobility.simpleMove6DOF() commands to send waypoint commands to Astrobee API
    Formation flight maneuvers can be repeated using Astrobee synchronization and native metrology
    At end of maneuver, data file downloaded to GDS

## Slide 41: Conversion of SVGS to run on HLP Updated SVGS APP with a simpler structure
Best way to run SVGS App without video output, is to change the main structure of SVGS App:
remove all unnecessary activities
Convert necessary activities to services
Make sure services from original SVGS still work
Updated SVGS APP:
  “Headless” SVGS: there are no activities  no GUI
  All user communications are performed via GDS
  Includes GS Library and Astrobee API  it can interact with Astrobee.

## Slide 42: Headless SVGS - Beta Version
Beta version of SVGS APK released at GitLab
User guide Rev 1 has been completed:
  Download the code
  Build the code
  Install the APP
  Start the APP
  Change SVGS setting
SVGS has been modified to run on Astrobee
  No output to screen
  Touchscreen not available for user input
  Services and Activities not used had to be removed
SVGS APP function checks received GDS commands and only executes command if all requirements are met.

## Slide 43
Sci Cam image
Guest Science APK
Trajectory
Find blobs
Calculate 6-DOF vector
Transformation to desired frame of reference
Nav. file
Desired waypoint
Save Astrobee Kinematic Data + SVGS Data to file @ 20 Hz
To Astrobee’s API
Guest Science Manager
L2 – Software Integration expanded
6-DOF Error
Instruction
Dump results data
From Guest science APK
To Guest Science APK

## Slide 44
Guest Science APK
Guest Science Library
Guest Science Manager
From Guest science APK
To Guest Science APK
Config.
Start
Trajectory
Instruction
Stop
Astrobee API
Sci Cam image
Nav. File
q (a, b, c, d)
(x, y, z,)
L1 – Software Integration- SVGS Mission APK
GDS
Camera settings
Operating limits

## Slide 45
Guest Science APK
Guest Science Library
Guest Science Manager
From Guest science APK
To Guest Science APK
Config.
Start
Trajectory
Instruction
Stop
Astrobee API
Sci Cam image
Nav. File
Contains maneuver waypoints
Image size, blob color, lighting settings, etc.
Timestamp, 6-DOF vector solution, Astrobee’s kinematics vector @ END OF MANEUVER
Stream of 1920x1080x3 matrices @ TBD frequency
q (a, b, c, d)
(x, y, z,)
L1 – Software Integration expanded w/notes
GDS
Keyword as String datatype
(x, y, z)
q (a, b, c, d)
Point datatype
JSON Object
Single command to be executed
4-element array of Quaternion datatype @ TBD frequency
3-element array of Point datatype @ TBD frequency
JSON Object
Camera settings
Camera name: string
Resolution: string
Frame rate: float
Bandwidth: float
Operating limits
Flight mode: string
Linear vel.: float
Linear acc.: float
Angular vel.: float
Angular acc.: float
Collision distance: float

## Slide 46
Guest Science APK
Guest Science Library
Guest Science Manager
From Guest science APK
To Guest Science APK
Config.
Start
Trajectory
Instruction
Stop
Astrobee API
Sci Cam image
Nav. File
onGuestScienceStart
GuestScience.customGuestScience
q (a, b, c, d)
(x, y, z,)
L1 – Software Integration expanded w/functions
GDS
Mobility.simpleMove6DOF
Mobility.simpleMove6DOF
Camera settings
Settings.setCamera
Operating limits
Settings.setOperatingLimits
onGuestScienceCustomCmd
onGuestScienceStop

## Slide 47: Location of SVGS Targets within ISS
CAD view of JPM
Will use seat tracks on panel wall to attach SVGS targets

## Slide 48
1 – Fixed Target Maneuver
    SVGS target fixed on wall
    SVGS reading used by Astrobee to generate waypoint commands
      Start at 2 m. , hold position and attitude
      Start at 2 m. , move 0.25 m towards target
      Start at 1 meter away
        Back away to 2 m, come back to 1 m
        Move laterally +/- TBD meters and hold position, return to 1 meter range
        At 1 m range, change roll, pitch, yaw +/- TBD degrees and hold position and attitude
48

## Slide 49: 2 - Leader – Follower Maneuver
“Leader” Astrobee performs prescribed 6DOF trajectory w.r.t. wall-mounted target. “Follower” Astrobee follows the leader at a fixed distance
2. Leader/Follower hold a fixed position and attitude and hold it
3. Repeat (1) and (2) for different range distances (0.25, 0.75, 1.0, 1.5 m)

## Slide 50
3 Single Vehicle Path Following
Astrobee travels from near coaxial position in front of Target 1 to Target 2, 3, 4, where it stops and holds position.
Targets 1 and 4 are blue LEDs
Target 2 is red LED
Target 3 is green LED
50

## Slide 51
4 Two-vehicle Formation flying path following
    Leader performs path following (Maneuver 3) while Follower follows at a prescribed distance (1 m) while holding formation
51

## Slide 52
5 . Multi-vehicle formation flight demo
52
    Leader performs path following w.r.t. wall-mounted target
    Follower follows leader at a fixed distance while holding formation
    Leader/Follower hold a fixed position and attitude and hold it

## Slide 53: Mission Timeline – Milestones
  SVGS Payload integration Kickoff meeting: 19 Jan 2021
  Hardware/design/development: 16 March 2021
  manufacture/ procurement (Rev 7) flight units: 28 April 2021
  Phase I Safety Review – Passed 11 May 2021
    Software Memo submitted to HIS 12 May 2021
  Hardware delivered to JSC: 21 June 2021
  VERITAS requirements submitted 08 June 2021
  HFIT + FIT of flight units at JSC 30 June 2021
  Modified SVGS delivery to ARC to test on Astrobee 30 June 2021
  EMC compliance (JSC): exemption approved
  Combined Phase II/III after HFIT + FIT (21 July ??)
  OZ POWR Review 29 July 2021
  Target Ops Start: Jan-Feb 2022

## Slide 54
Summary
54
SVGS Payload and SVGS Mission Objectives have been presented:
  SVGS Electrical, mechanical and software interfaces with Astrobee
  CONOPS and on-orbit activities for SVGS
Other payload requirements have been outlined
Proposed five maneuvers will be further refined
Mission Schedule
Delivery of SVGS flight units to JSC for HFIT, FIT, EMI Testing: 24 June 2021
  Proposed flight: Crew-3. Delivery date: 8/16/2021, Launch date: 10/31/2021