## Slide 1
Space Technology Mission Directorate
Game Changing Development Program
Jason Schuler | Drew Smith | FY22 ISRU Pilot Excavator (IPEx) Annual Review Presentation | 09.13.22
Jason Schuler/jason.m.schuler@nasa.gov

## Slide 2: Project Overview
Technology Product Capability:
  Robotic excavation technology
Technical Capabilities:
  Low gravity excavation
  Lunar surface system reliability – Distance traveled quantity regolith excavated/delivered
  Dust tolerant battery charging
  Dust tolerant thermal control
  Supervised autonomous operation
Exploration & Science Applicability:
  Supports ISRU and In-Situ Construction as an enabling technology to allow sustainable missions on the Moon and other extraterrestrial bodies
  Excavation supports scientific investigations related to surface and sub-surface regolith.

## Slide 3: Team Members / Project Org Slide
Primary GCD Interfaces
GCD Program Element Manager
Eugene Schwanbeck (JSC)
GCD Acting Program Manager
David Moore (LaRC)
WBS 596118.04.65.76 – KSC Lead Center
PjM: Jason Schuler
DPjM: Jenna Fothergill
WBS 596118.04.65.72
JSC Support Center
POC: Bill Bluethmann
WBS 596118.04.65.55
Contract – JPL Support Center
POC: Hari Nayar
SBIR Phase III Contract – Astrobotic Technologies, Inc. – Industry Support Partner
POC: John Landreneau
Team Member Roles | 
Principal Investigator / Project Manager | Jason Schuler
Deputy Project Manager | Jenna Fothergill
Systems Engineer | Jeffrey Dyas
Lead Mechanical Engineer | Drew Smith
Lead Controls Engineer | Andrew ‘AJ’ Nick
Lead Software Engineer | Brad Buckles
Bucket Drum Subsystem Lead | Nathan Gelino
Software Engineer | Kurt Leucht
ISRU Senior Consultant | Rob Mueller
Mechanical Engineer | Musashi Howe
Notes: If you have submitted a Project Plan, you could utilize the Organizational Chart found in section 8.3 – Management Structure

## Slide 4: Mission Infusion & Partnerships
Contributing partners and/or stakeholders:
  NASA Centers – KSC, JPL, JSC
  Industry: Astrobotic Technology
KSC
Astrobotic
JPL
JSC
Infusion/transition plan:​
  CLPS CT-1: Supply regolith to ISRU O2 Demo​
  Inform future excavator design to support ISRU Pilot Plant. Performing excavation to supply the plant with feedstock.
Additional infusion:
  Future excavation for ISRU and excavation for construction needs for Lunar and Martian surface missions.​
  The ISRU Pilot Excavator technology has potential to be transitioned to additional government or commercial use. A bucket drum excavator patent has been awarded to NASA and already licensed to 6 companies.

## Slide 5: Project Goals & Project Objectives (1 of 2)
Technology Goals | 
Goal #1 | Technology Development Phase: Design and build a flight ready robotic system to demonstrate loose granular lunar regolith excavation, transport, and delivery at a scale required for an in-situ pilot processing plant.
Goal #2 | Flight Demonstration Phase: Support the integration, flight operations, and reporting of the lunar surface demonstration.
Project Objectives ​ | 
Objective #1​ | Define Concept of Operations and requirements for a 30kg–class pilot excavator to be demonstrated on a lunar polar CLPS mission.​
Objective #2​ | Complete trade studies and analyses of high-risk excavator components and subsystems (thermal control, autonomous navigation aids, bucket drum geometry, dust mitigation, battery charging, etc.)​
Objective #3​ | Design and build the IPEx Brassboard subsystems (actuators, thermal control, avionics, etc.) and test in relevant environment raising them to TRL5.
Objective #4​ | Assemble IPE Brassboard Unit and perform a full mission length ground demonstration.

## Slide 6: Project Goals & Project Objectives (2 of 2)
Project Objectives ​ | 
Objective #5​ | Build two identical IPEx units, a Prototype Qualification Unit (PQU) and Prototype Flight Unit (PFU), and test systems to qualification and acceptance levels, respectively.
Objective #6​ | Complete a full mission length ground demonstration of the IPEx Prototype Qualification Unit.
Objective #7​ | Deliver IPEx Prototype Flight Unit to CLPS provider and integrate into lander.
Objective #8 | Complete an 11-day flight mission demonstration of the IPEx Prototype Flight Unit on the lunar surface.
Objective #9 | Document mission performance, lessons learned and overall project summary in post-flight, project closeout report.

## Slide 7: ISRU Pilot Excavator Technology Maturation Schedule
Project Plan baseline schedule shown. CR to follow to shift FY23+ milestones.
FY23+ milestones will shift right ~4months due to budget constraints
FY22 Highlights
Completed high-risk subsystems trade study report (K3)
GCD Project Plan approved (KDP2)
Completed SRR (C2)
Completed SRR and PDP review for Blue Origin Suborbital experiment
Astrobotic SBIR Phase III contract mod approved.
Notes: Note – K5 does not shift
KDP = Key Decision Point

## Slide 9: Concept of Operations Flow Chart
Drive to dig site unloaded
(5.55 minutes)
Excavate
(2.12 minutes)
Dump
(0.37 minutes)
Drive to dump site loaded
(5.55 minutes)
Repeat ~16x
Total Time
3.6 hours (216 minutes)
Recharge Battery
(136 minutes)
Thermal Reset
(121 minutes)
Thermal Reset
(121 minutes)
Repeat 21x
Mission Ops Durations (hours) |  |  |  | 
Deployment | Mapping | Operational | Margin | Total
8 | 18 | 208 | 30 | 264
Battery < 30%? or
PCM saturated?
YES
NO

## Slide 10: FY22 Accomplishments: Astrobotic Partnership
Continued work with Astrobotic on the interface control document for the Integrated Avionics Unit (IAU)
Completed a draft layout of carrier board with locations for wire connections.
Modification to Astrobotic contract in-work. This mod will further develop/integrate avionics/software through the IPEx Brassboard Unit ground demo (Summer 2023).
Engineering Units of the Astrobotic/Wibotic wireless charging system are on order for TRL 5 testing and ground demo
Wibotic Wireless Charger Antennas
IPEx Breadboard Unit with Astrobotic CubeRover

## Slide 11: FY22 Accomplishments: Bucket Drum Testing
Performance Testing to Inform Bucket Drum Design
  Location: KSC Swamp Works regolith testbed – BP-1 lunar regolith simulant
  Test area leveled, compacted, and characterized with geotechnical measurements
  Purpose to determine the forces in various scale bucket drums for excavator design
  Varied rotation speed, linear speed, drum size, cut depth
  Paper submitted/presented at ASCE Earth and Space 2022
X
Z
R
~3.85m excavation area

## Slide 12: FY22 Accomplishments: Bucket Drum Simulations
EDEM simulation of bucket drum
EDEM simulation calibration
EDEM Simulation of alternate bucket drum geometry
EDEM reduced gravity bucket drum simulation
Completed calibration testing of BP-1 regolith for EDEM discrete element modeling simulation (angle of repose and inclined plane)
Altair completed initial 12-day simulation run
In-house simulation capability setup to iterate on bucket drum geometry.

## Slide 13: FY22 Accomplishments: Bucket Drum Lunar-G Suborbital Experiment
Bucket Drum Lunar-G Suborbital Experiment Section Layout (1 of 2)
Experiment to measure the regolith flow rate inside a bucket drum at vacuum and lunar-g.
Variables: Baffle geometry, Regolith simulant, RPM
Will validate DEM simulations
5 bucket drum sections, 1 dynamic angle of repose
Completed SRR on 7/12. Decision made to switch from 1 double locker to 2 single lockers.
Completed Preliminary Payload Design Package (PDP) Review with Blue Origin on 7/27.
Flight: Q1 CY2023.
Baseline baffle geometry (left) and variables (right)

## Slide 14: FY22 Accomplishments: Rock Clearing
Tested a new option for moving large and embedded rocks by flipping the rotational direction of the bucket drums.

## Slide 15: FY22 Accomplishments: Actuator Design and Testing
Assembly of shoulder motor
T-Vac Cold-head
Hall effect feedback motor testing
Arm motor testing in t-vac dynamometer
Actuator Development/Testing:
Resolved motor control issue by increasing the Pulse Width Modulation (PWM) control loop frequency on alternate motor controller. Implementing firmware change for flight forward motor controllers.
Motor controller vender ESI supplied custom firmware to run the motor controller at 40kHz.
Mounted a motor with hall sensor feedback in the thermal-vacuum (t-vac) dynamometer test stand & tested velocity control with hall sensors only.
Worked with motor vendor ThinGap to identify 2 motor options with custom hall sensor feedback for use on the arm and bucket drum actuators. Procurement in process.
Ran several motor characterization tests in t-vac dynamometer including no load tests at various temperatures, loaded tests from –70 C to +50 C.
Began assembly of the harmonic stage and reconfiguration of the t-vac dynamometer chamber to move to harmonic testing
Upgraded the t-vac dynamometer test chamber to include thermal monitoring and system override to protect the cryocooler cold head from exceeding maximum temperature. This will allow for hot and cold around-the-clock test capability.

## Slide 16: FY22 Accomplishments: Thermal Analysis and Design
Sensitivity to radiator area and PCM melt temperature
Completed a trade study of the con-ops timing sensitivity to radiator size, phase change material (PCM) mass, and PCM melt temperature. Reduced radiator size and PCM mass may be possible from baseline assumptions.
Completed analysis of impact of increased actuator power due to lower-than-expected actuator efficiency. An increase from 4W to 30W (average) would not significantly affect the mission timeline.
Cumulative excavate-charge cycles over mission duration

## Slide 17: FY22 Accomplishments: Thermal Analysis and Design
Began detailed thermal control system design
Actuated radiator cover to protect from dust. Only opened when IPEx is stationary.
Phase Change Material (PCM) absorbs thermal energy while radiator cover is closed.
Thermal resets required before and after battery charges: IPEx stationary – Radiator cover opens – PCM re-solidifies via conduction to radiator.
Sensitivity to radiator area and PCM melt temperature
Actuated Radiator Cover
Radiator
Batteries
Battery Charger
IAU and Heat Spreader
Phase Change Material

## Slide 18: FY22 Accomplishments: Cameras
Notional camera locations
IPEx baseline design includes 8 cameras:
2 stereo camera pairs/4 mono cameras
6 of the cameras are in fixed body-mounted locations
2 of the cameras are mounted on the arms between the bucket drums
Each camera will have an electrostatic dust shield (EDS) attached to a one-time deployable clear lens cover (based on VIPER design)
High camera count enabled by low-cost flight qualified machine vision cameras supplied by Astrobotic as CubeRover heritage hardware
VIPER NAV Lens Cap
EDS dust clearing before (left) and after (right)
FLIR Blackfly

## Slide 19: FY22 Accomplishments: Cameras
Vision System Maturation
Created a simulation in Unity with realistic lunar terrain provided by JPL
Met with Electrodynamic Dust Shield (EDS) team to discuss dust mitigation & use of EDS for camera lens covers.
Baseline plan for camera locations developed. 8 cameras total
Camera view below the shoulder joint
Camera view between the bucket drums
EDS Lens Cover Released
Concept Camera Module

## Slide 20: FY22 Accomplishments: Navigation
Example Rock Sizes, Hazards, and Mitigations
Rock and Crater Hazard Map
Generated maps of statistical rock and crater distributions and traversal limits based on mobility restrictions of the rover to inform navigation requirements.
Evaluating down-selected autonomous navigation techniques for sensitivity to drive speed and harsh lighting conditions.

## Slide 21: FY22 Accomplishments: Lunar Surface Visualization Simulation
Unity Simulation of Mission Lighting
Stowage and deployment simulation
Site camera view of excavation zone
VR configuration for visualization tool
Lunar Surface Visualization tool using Unity simulator software
1km x 1km section of actual Lunar Reconnaissance Orbiter 5-meter resolution surface data. Detailed craters/rocks added to surface by JPL team.
Visual markers on ground to show the digging area and the 100-meter circumference circle around the lander
20 camera views to choose from: 10 site cameras and 10 onboard robot cameras. Onboard cameras have accurate resolution & field of view
Automated robot traversal of 100-meter circumference around lander
Spin-off CIF project to further develop and merge with other sims.

## Slide 22: FY22 Accomplishments: Auto-Dig
Best-fit model planes with RASSOR 2 torque/current test data
Autodig User Interface
Updated the ROS 2 version of the RASSOR 2.0 software to include AutoDig routines and began testing in the KSC Regolith Test Bed.
Updated the control strategy of Auto-Dig routine. Implemented method to estimate regolith in drum in real-time during excavation.
Created models of the torque vs current for RASSOR 2 actuators and validated with tests using RASSOR 2. This will be used to convert current readings to actual torque feedback.
A test was conducted where a range of masses to collect was commanded. The excavator automatically stops when it reaches its target. The actual collected regolith was weighed and plotted
Presented Auto-Dig progress at the 2022 Space Resources Roundtable. Preparing a full paper for the 2023 IEEE Aerospace conference.

## Slide 23: FY22 Accomplishments: Auto-Dig

## Slide 24: FY22 Accomplishments: Wheels
Updated 12” Wheel Design Concept
Wheel development:
Continued with wheel design & updated analysis model in NX Nastran
Installed new sheet metal wheels based on VIPER design on RASSOR 2
Began development of scaled (12”) wheel design. Considering switching to machined parts from sheet metal for weight savings.
17” Sheet Metal Wheel

## Slide 25: FY22 Accomplishments: Excavator System Layout
Continued evolution of overall IPEx CAD layout.
All major subsystems have defined volume envelopes.
Iterated on the thermal control system layout and concluded with a version that allows for a very wide range of motion for the IPEx arms and bucket drums.
Currently focusing on the concept chassis and structure for the avionics enclosure.
Concept Layout Progression
Current Design

## Slide 26: Project Assessment Summary
Project Name | Performance |  |  |  | Comments
 | C | S | T | P | 
Mid Year |  |  |  |  | Technical – High risk subsystem trade study completed; mitigations identified. Cost – Current budget shortfall due to continuing resolution may impact deliverables. Some procurement contracts are being put on hold due to lack of certainty in remaining budget the project will receive. Schedule – Current budget shortfall due to continuing resolution may impact deliverables. Some procurement contracts are being put on hold due to lack of certainty in remaining budget the project will receive. If full planned budget is not received, some deliverables will slip right. Programmatic – No Issues
Annual |  |  |  |  | Technical – Detailed design and analysis showing positive margin to meet KPP goals. Cost –FY22 budget shortfall has impacted planned deliverables. Some procurements were delayed/put on hold until additional funding available. Schedule – FY22 budget shortfall has impacted baseline planned milestones. Some procurements were delayed/put on hold. Remaining project milestones are likely to slip approximately 4 months. Programmatic – No Issues
Notes: Is this yellow (project control) or red (program control)
Can make green if full budget received in future years and milestones adjusted based on impacts

## Slide 27: Plans Forward and Transition / Infusion Plan
Forward Plans:​
  Complete design and tests of subsystems (actuators, thermal control, avionics, etc.) in a relevant environment, advancing them to TRL5 (K4) – FY23
  Deliver bucket drum flight experiment for Blue Origin Lunar-G Flight (K5) – FY23
  Perform brassboard system level excavation demonstration​, advancing system to TRL5 (K6) – FY23
  Incorporate lessons learned from TRL 5 test into TRL 6 design/fabrication
  Perform system level TRL 6 excavation demonstration​
Commercialization/Infusion Plans:​
  ​Targeting CLPS CT-1 Mission supplying regolith to ISRU O2 Demo in lunar south-pole region.
  Close coordination with ISRU teams for ISRU Pilot Plant integration. ​
  Supporting licensing efforts. 6 companies to-date have received licenses for use of the counter rotating bucket drum technology.
Notes: Infusion: An investment reaches a conclusion where a technology is handed off for use by a mission or other need. Infusions can be made to other NASA Mission Directorates, other Government Agencies, Commercial Entities, or International Partner.
Transition: An investment reaches a conclusion where a technology is handed off for further development. Transitions can be made to other STMD programs, other NASA Mission Directorates, academic institution, other Government Agencies, Commercial Entities, or International Partner.

## Slide 28: Education/Public Outreach
EPO Involvement
Discovery Channel NASA innovation video shoot & interview of Jason Schuler about IPEx - 10/4/21
IPEx/RASSOR talk & demonstration at a local middle school - Nov 2021
HUNCH kickoff at Eau Gallie High School with RASSOR live demo - 12/9/2021
HUNCH program students at Eau Gallie High School assembled IPEx wheels – May 2022
NASA Lunabotics Competition support & virtual session with finalists – May 2022
Publicly releasable CAD model of RASSOR uploaded to the NASA 3D Resources website: https://nasa3d.arc.nasa.gov/detail/RASSOR
Partnership with the University of Central Florida to support development of the bucket drums experiment for Blue Origin Lunar-G flight in 2023.
Discovery Channel Interview
Middle School Presentation/Demo
EGHS HUNCH Program – Students Assemble IPEx Wheels
Notes: Summary of the EPO activities (papers, conferences, outreach events) participated in over the last 6 months and the forward outlook for 6 months

## Slide 29: Education/Public Outreach
EPO Involvement
ASCE Earth and Space Conference presentation on scaled bucket drum testing, April 2022
Space Resources Roundtable presentation on AutoDig algorithm development, June 2022
Developed a bucket drum demonstration for GCD public affairs to take to various conferences and events, April 2022
Professional video/photography of RASSOR captured with simulated lunar lighting conditions in KSC GMRO Regolith Test Bed. Imaged shared with millions on NASA Instagram page, Aug 9.
6 Month Look-Ahead | 
Continued partnership with UCF for bucket drum experiment development for Blue Origin Lunar-G flight in 2023 | Q1 CY23
K5 Milestone Blue Origin Flight Lunar–G Test of Bucket Drums | Q1CY23
AutoDig Software Paper/Presentation at IEEE Aerospace Conf | March 2023
ASCE Earth & Space Conference Paper/Presentation | April 2023
EPO Calendar Outlook (High Priorities):
IPEx Shared on NASA Instagram
EPO Bucket Drum Demo Display
Notes: Summary of the EPO activities (papers, conferences, outreach events) participated in over the last 30 days and the forward outlook 30-60 days

## Slide 30: Summary
Major accomplishments for the Year:
Established internal cleaning/grease plating capability​
Made significant progress on thermal control system design, including incorporation of actuated radiator cover & phase change material
Began testing of TRL 5 actuators in relevant environment​
Selected motors and feedback sensors for arm and bucket drum actuators​​
Updated the RASSOR 2.0 control software to ROS 2, overhauled AutoDig routines, and began testing in the KSC Regolith Test Bed
Selected baseline camera configuration​
Completed bucket drum testing & presented paper to 2022 ASCE Earth & Space Conference ​
Key Decision Point 2 Completed – Project Plan Approved
Key Milestone 3 - High-risk subsystems trade study report completed
Controlled Milestone 2 - Systems Requirements Review (SRR) completed
Completed SRR and Preliminary Payload Design Package (PDP) review for Blue Origin suborbital flight experiment
Established contracts with Astrobotic Technology to develop/deliver avionics units and wireless charging systems.
TechMat Capability End State​
TRL7 CLPS demonstration of robotic excavation of 10t of regolith on the lunar surface
Enabling technologies: ​
Low gravity excavation system ​
Robust Lunar surface system reliability ​
Dust tolerant battery charging​
Dust tolerant thermal control​
Supervised autonomous operation

## Slide 31: Questions?
Questions?